IV

FIG International Gymnastics Federation

IV Testing Procedures

01.01.2006

1

Contenu:

Le chapitre suivant contient les descriptions détaillées et techniques des méthodes d'essai pour les

agrès gymnastiques pour lesquelles l'essai par une laboratoire de test officielle de la FIG est obliga-

toire. Concernant la codification des agrès, les mêmes abréviations comme dans chapitre II sont

utilisées.

Comme ces explications s'adressent surtout aux autorités de la FIG, aux techniciens/-iennes, ingé-

nieurs (femme), scientifiques de sport et aux laboratoires de test et départements de développement

des firmes, elles sont formulées qu'en anglais.

IV-1

IV-2

Sommaire des agrès avec abréviations, date de publication et équivalences éventuelles

concernant les méthodes d'essai

Spécifications de standard pour les agrès individuels

Contents:

Chapter IV comprises the detailed technical descriptions of the test procedures for those gymnas-

tics apparatus for which a test at an official FIG test laboratory is obligatory. For identification of

apparatus the same abbreviations as in chapter II are used.

Since the following explanations are primarily intended for FIG authorities, technicians, engineers

and sports scientists, as well as for test laboratories and research departments of companies, they

are published in English exclusively.

IV-1

IV-2

Overview of the gymnastics apparatus, with abbreviations, date of publication and pos-

sible common test features

Standard specifications for individual gymnastics apparatus

Inhalt:

Das folgende Kapitel IV umfasst die detaillierten, technischen Beschreibungen der Prüfverfahren

für diejenigen Turngeräte, für die eine Prüfung an den offiziellen Prüfinstituten der FIG vorge-

schrieben sind. Bei der Kennzeichnung der Turngeräte werden die gleichen Abkürzungen wie in

Kapitel II verwendet.

Da sich die Ausführungen ausschließlich an FIG-Behörden, Testinstitute, Techniker, Ingenieure,

Sportwissenschaftler und Entwicklungsabteilungen in Firmen richten, sind sie nur in Englisch ab-

gefasst.

IV-1

IV-2

Übersicht über die Turngeräte mit Abkürzungen, Erscheinungsdatum und eventuellen

Äquivalenzen bezüglich der Prüfverfahren.

Normspezifikationen für die einzelnen Turngeräte

IV

FIG International Gymnastics Federation

Overview of the gymnastic apparatus with obligatory Tests

at FIG Test - Institutes

01.01.2006

2

MAG

Apparatus

Floor

Pommel Horse

Rings

Vaulting Table

Parallel Bars

High Bar

Landing Mat 20cm

Landing Mat 10cm

Vaulting Board

Code

MAG1

MAG2

MAG3

MAG4

MAG5

MAG6

MAG11

MAG12

MAG14

Code

WAG1

WAG2

WAG3

WAG4

WAG11

WAG14

Code

RG1

Date of Issue Equivalence

01.01.06

01.12.94

1989

01.02.01

01.01.97

29.03.96

01.08.96

12.07.89

01.01.06

WAG4; ACRO1

WAG1

WAG11; ACRO11

WAG14; TRA15

WAG

Apparatus

Vaulting Table

Uneven Bars

Balance Beam

Floor

Landing Mat 20cm

Vaulting Board

Date of Issue Equivalence

01.02.01

01.05.93

01.12.94

01.01.06

01.08.96

01.01.06

MAG4

MAG1; ACRO1

MAG11; ACRO11

MAG14; TRA15

RG

Apparatus

Floor

Date of Issue Equivalence

01.12.92

AER

Apparatus

Floor

Code

AER1

Date of Issue Equivalence

01.07.2000

IV

FIG International Gymnastics Federation

Overview of the gymnastic apparatus with obligatory Tests

at FIG Test - Institutes

01.01.2006

3

TRA

Apparatus

Trampoline

Tumbling Track

Vaulting Board

Code

TRA1

TRA3

TRA14

Date of Issue

01.02.1995

01.07.1996

01.01.2006

Equivalence

MAG14; WAG14

ACRO

Apparatus

Floor

Landing Mat 20cm

Code

ACRO1

ACRO11

Date of Issue

01.01.2006

01.01.2000

Equivalence

MAG1; WAG4

MAG11; WAG11

IV

4

FIG International Gymnastics Federation

Standard Specification for Floors

MAG – Men Artistic Gymnastics

Standard Specification: Floors for Men Artistic Gymnastics

IV

MAG 1

01.01.2006

1

This standard is issued under the fixed designation FIG: IV-MAG1-01.01.1997; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of floors and to

minimize any differences between competition and

training equipment.

1 Scope

1.1 This specification covers the measurement of

certain shock-absorbing characteristics, the impact

force - time relationships, and the rebound properties

of gymnastic floors. This standard specification is ap-

plicable to all gymnastic floors that are to be used at

any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a gymnastic floor

which complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG1.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Base plane: The starting reference plane of

the gymnastic floor from which the total deflection

and total height of rebound is determined. It is taken

as the top plane of the gymnastic floor.

3.1.3 Deflection: The measured distance (in mm)

between the base plane and the maximum displace-

ment of the impactor below the base plane.

3.1.4 Force (F): The product of the mass of the im-

pactor, expressed in kg, and the acceleration of the

impactor, expressed in m/s2.

3.1.5 Maximum Force (Fmax): The maximum value

of force measured during the impact and expressed in

Newtons.

3.1.6 Height of rebound: The measured distance (in

mm) between the base plane and the maximum dis-

placement of the impactor above the base plane.

3.1.7 Impactor: The striking part of the test appara-

tus.

3.1.8 Impact velocity: The velocity of the impactor,

expressed in m/s, immediately prior to crossing the

base plane on impact.

3.1.9 Theoretical drop height: A calculated drop

height which equates the measured velocity of the im-

pactor at the moment of impact to a height that would

generate the same velocity if the test were performed

at sea level and there was no friction to retard the im-

pactor during a drop from that height.

4 Principle of Measurement

4.1 A test specimen is impacted at a specified ve-

locity with an impactor of given mass and geometry.

A transducer mounted in the impactor monitors the

acceleration – time history of the impactor which is

recorded with the aid of a data acquisition system. An

additional transducer may be used to monitor the dis-

placement – time history of the impactor.

4.2 Dynamic data obtained during these procedures

are indicative of the cushioning and rebound proper-

ties of the gymnastic floor and materials used in train-

ing and FIG-sanctioned competitions.

5 Performance Requirements

5.1 When tested according to the procedures de-

scribed in Section 9, the overall mean values of the

measured variables across all impact sites shall be

within the figures of Table 1.

Table 1: Figures for Gymnastic Floors

x represents the mean value of the measured variable

Deflection

(mm)

69.5 ≤x ≤

Height of rebound

(mm)

245 ≤x ≤335

Fmax

(N)

x ≤4500

FIG International Gymnastics Federation

Standard Specification for Floors

MAG – Men Artistic Gymnastics

6 Test Apparatus

6.1 Impact test machine: Any type of dynamic test-

ing apparatus that is capable of impacting a test

specimen at a prescribed impact velocity and monitor-

ing and recording the acceleration - time history of

the impactor is acceptable. The impact test machine

and the impactor shall have sufficient rigidity to

eliminate undesirable vibrations in the apparatus

which might be recorded on the acceleration - time

curve. The impact test machine shall also be designed

in such a manner that only the impact face contacts

the test specimen at any time during the test proce-

dures.

6.2 Impactor: The impactor shall be 20 kg ±0.2 kg

and shall have a flat impact face with a 10 cm ±

0.5 cm diameter. The edge of the impactor face

should be relieved to eliminate sharp edges. Provision

shall be made so that the accelerometer can be se-

curely fastened parallel to the vertical axis of the im-

pactor with a maximum deviation of ±5o.

6.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.3.1 Acceleration - time: The selection of the spe-

cific acceleration - time recording equipment, includ-

ing transducers and recorders, is at the discretion of

the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the peak acceleration value to an accuracy of ±5% of

the true value. The total system, detection and re-

cording, shall be capable of measuring impact accel-

erations of up to 200 g at frequencies from 2 to

1000 Hz to an accuracy of ±5%. The minimum sam-

pling rate of the data acquisition system shall be 5000

Hz.

6.3.2 Displacement - time: It is optional, but desir-

able, that the displacement - time history is recorded

by a separate transducer. Any transducer that provides

a linear signal proportional to the displacement of the

impactor along the impact axis which can be moni-

tored simultaneously with the acceleration - time trace

is acceptable. If displacement is recorded, the test

equipment shall have means to determine and record

the top plane (base plane) of the test specimen from

which the total deformation and rebound height are

determined.

6.3.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

7 Test Specimen

7.1 The test specimen submitted for testing shall

IV

MAG 1

01.01.2006

2

represent the gymnastic floor as it is intended to be

used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG1. Exception: See 7.3.

7.3 The minimum horizontal dimensions (length *

width) for any test specimen shall be 200 cm * 120

cm.

8 Conditioning and Test Temperature

8.1 Test specimens shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 Impact locations: A total of nine impact sites

shall be designated on the test specimen. See Figure 1

for an illustration of the impact sites.

Figure 1: Impact Locations for Gymnastic Floors

9.2 Impact test procedures:

9.2.1 Place the test specimen under the impact test

machine on a smooth, solid floor (concrete or metal

plate) and orient the impactor such that the centre of

the impact face will contact one of the designated im-

pact test sites.

9.2.2 Raise the impactor to an appropriate drop

height such that it will contact the test specimen with

an impact velocity of 3.96 m/s ±3%. This corre-

sponds to a theoretical drop height of 0.8 m.

9.2.3 Release the impactor and capture the accel-

eration - time history and displacement - time history

(if applicable) using recording equipment described in

Section 6.3.

9.2.4 Upon completion of a given impact test, raise

the impactor off the surface of the test specimen.

9.2.5 The duration between tests at a given impact

site shall not be less than 120 seconds.

9.2.6 Each test specimen shall receive a total of 90

impacts. Impact each of the nine impact sites ten

times.

FIG International Gymnastics Federation

Standard Specification for Floors

MAG – Men Artistic Gymnastics

9.3 Calculations:

9.3.1 Immediately following each test, record the

following measurements: Fmax (N), Deflection (mm)

and Height of rebound (mm).

9.3.2 The last eight tests for each impact site shall

be used to determine the arithmetic mean value of a

measured variable for each impact site and for the

overall mean value of a measured variable across all

impact sites.

9.3.3 Calculate the mean values of Deflection,

Height of rebound and Fmax across all impact sites

rounded to zero decimal places.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested gym-

nastic floor, including type, source, manufacturer’s

model number (if appropriate), dimensions of test

specimen, and any other pertinent information. Pho-

tographs may be included in the test report for sample

documentation purposes.

IV

MAG 1

01.01.2006

3

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Description of the impactor mass and the

drop height conditions.

10.1.6 Description of the test results relative to the

performance requirements identified in Section 5.

10.1.7 Mean values of Deflection, Height of re-

bound and Fmax across all impact sites.

10.1.8 Maximum value, minimum value and stan-

dard deviation of Deflection, Height of rebound and

Fmax variables.

10.1.9 Mean values of Deflection, Height of re-

bound and Fmax for the last eight tests at each impact

site.

10.1.10 Deflection, Height of rebound and Fmax val-

ues for all tests.

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

4

FIG International Gymnastics Federation

Standard Specification for Pommel Horses

MAG – Men Artistic Gymnastics

IV

MAG 2

01.12.1994

1

Standard Specification: Pommel Horses for Men Artistic Gymnastics

This standard is issued under the fixed designation FIG: IV-MAG2-01.12.1994; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of pommel

horses and to minimize any differences between com-

petition and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain shock-absorbing and frictional characteristics

of pommel horse bodies, as well as positional stability

and frictional characteristics of pommels. This stan-

dard specification is applicable to all pommel horses

that are to be used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a pommel horse which

complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG2.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Base plane: The starting reference plane of

the horse body from which the total deflection and

total height of rebound is determined. It is taken as

the top plane of the horse body.

3.1.3 Deflection: The measured distance (in mm)

between the base plane and the maximum displace-

ment of the impactor below the base plane.

3.1.4 Force (F): The product of the mass of the im-

pactor, expressed in kg, and the acceleration of the

impactor, expressed in m/s2.

3.1.5 Maximum Force (Fmax): The maximum value

of force measured during the impact and expressed in

Newtons.

3.1.6 Height of rebound: The measured distance (in

mm) between the base plane and the maximum dis-

placement of the impactor above the base plane.

3.1.7 Impactor: The striking part of the test appara-

tus.

3.1.8 Impact velocity: The velocity of the impactor,

expressed in m/s, immediately prior to crossing the

base plane on impact.

3.1.9 Theoretical drop height: A calculated drop

height which equates the measured velocity of the im-

pactor at the moment of impact to a height that would

generate the same velocity if the test were performed

at sea level and there was no friction to retard the im-

pactor during a drop from that height.

3.1.10 Slider: A test body of given mass and ge-

ometry for measuring frictional characteristics of the

horse body. The slider includes a test sole which is

bonded to the bottom of the slider and is made of syn-

thetic material with defined friction properties.

3.1.11 Maximum traction force: Maximum force,

expressed in Newtons, applied during the pulling

movement of the slider.

3.1.12 Friction coefficient of horse body: Quotient

of the maximum traction force (in N) and the weight

of the slider (in N).

3.1.13 Displacement of pommels: Relative and

horizontal displacement (in mm) between a pair of

pommels at a defined horizontal stretching force.

3.1.14 Residual displacement of pommels: Residual

displacement (in mm) between the pommels after the

removal of the stretching force.

3.1.15 Testing belt: A belt for measuring frictional

properties of the pommels. The surface of the belt is

made of synthetic material of defined frictional prop-

erties.

3.1.16 Friction force of pommel: The friction force,

expressed in Newtons, generated by the contact of the

testing belt and the specimen pommel.

3.1.17 Friction coefficient of pommel: Quotient of

the friction force (in N) and the pulling-down weight

of the testing belt (in N).

FIG International Gymnastics Federation

Standard Specification for Pommel Horses

MAG – Men Artistic Gymnastics

4 Principle of Measurement

4.1 The complete test procedures include 4 parts:

Determination of shock absorption of horse body, de-

termination of top friction of horse body, determina-

tion of positional stability of pommels, and determi-

nation of friction of pommels.

4.1.1 Test A - Shock absorption of horse body: A

specimen horse body is impacted with an impactor of

given mass and geometry at a specified velocity. A

transducer mounted in the impactor monitors the ac-

celeration – time history of the impactor which is re-

corded with the aid of a data acquisition system. An

additional transducer may be used to monitor the dis-

placement – time history of the impactor.

4.1.2 Test B - Top friction of horse body: A slider is

pulled horizontally upon the surface of a specimen

horse body at a defined loading rate. A transducer

connected to the pulling cable monitors the maximum

traction force generated during the pulling movement.

4.1.2.1 Test C - Positional stability of pommels: A

pair of specimen pommels is stretched outward in the

horizontal direction at a defined stretching force. The

incremental displacement between the pommels dur-

ing the time of force application is monitored. Resid-

ual displacement between the pommels is also moni-

tored after the removal of the stretching force.

4.1.3 Test D - Friction of pommels: A testing belt is

hung on a specimen pommel and pulled down at a de-

fined weight. The frictional resistance force of the

pommel is monitored.

4.2 Data obtained during these procedures are in-

dicative of the cushioning properties and the top fric-

tion characteristics of the horse body and the posi-

tional stability and frictional properties of the pom-

mels used in training and FIG-sanctioned competi-

tions.

5 Performance Requirements

5.1 Test A – Shock absorption of the horse body:

When tested according to the procedures described in

Section 9.1, the values of the measured variables shall

meet the performance requirements specified in Ta-

ble 1.

5.2 Test B – Top friction of the horse body: When

tested according to the procedures described in Sec-

tion 9.2, the mean values of the measured variables

shall meet the performance requirements specified in

Table 2.

5.3 Test C – Positional stability of the pommels:

When tested according to the procedures described in

Section 9.3, the mean values of the measured vari-

ables shall be within the figures of Table 3.

IV

MAG 2

01.12.1994

2

Table 1: Figures for Test A – Shock absorption of the

horse body

See Figure 1 for an illustration of the impact sites.

x represents the mean values of the measured variables

Deflection

(mm)

Mean values

across impact

sites 1 to 5

Difference

between high-

est and lowest

mean values

on impact sites

1 to 5

Height of

rebound

(mm)

80 ≤x ≤205

Fmax

(N)

16 ≤x ≤

x ≤12000

≤16

≤130

≤2500

Table 2: Figures for Test B – Top friction of the horse

body

x represents the mean value of the measured variable

Friction coefficient of horse body

Mean value across

test sites 1 to 3

Difference between

highest and lowest

mean value on test

sites 1 to 3

Difference between

mean values of

orthogonal test

directions

0.35 ≤x ≤0.60

≤0.05

≤0.05

Table 3: Figures for Test C – Positional stability of the

pommels

x represents the mean values of the measured variables

Displacement of pommels (mm)

Residual displacement of pommels (mm)

x ≤15.0

x ≤1.0

Table 4: Figures for Test D – Friction of the pommels

x represents the mean value of the measured variable

Friction coefficient of pommel

Mean value of both

pommels

Difference between

two pommels

0.45 ≤x ≤0.80

≤0.05

FIG International Gymnastics Federation

Standard Specification for Pommel Horses

MAG – Men Artistic Gymnastics

5.4 Test D – Friction of the pommels: When tested

according to the procedures described in Section 9.4,

the mean values of the measured variable shall be

within the figures of Table 4.

6 Test Apparatus

6.1 Test A – Shock absorption of horse body:

6.1.1 Impact test machine: Any type of dynamic

testing apparatus that is capable of impacting a test

specimen at a prescribed impact velocity and monitor-

ing and recording the acceleration - time history of

the impactor is acceptable. The impact test machine

and the impactor shall have sufficient rigidity to

eliminate undesirable vibrations in the apparatus

which might be recorded on the acceleration - time

curve. The impact test machine shall also be designed

in such a manner that only the impact face contacts

the test specimen at any time during the test proce-

dures.

6.1.2 Impactor:Theimpactorshallbe

10 kg ±0.1 kg and shall have a flat impact face with a

10 cm ±0.5 cm diameter. The edge of the impactor

face should be relieved to eliminate sharp edges. Pro-

vision shall be made so that the accelerometer can be

securely fastened parallel to the vertical axis of the

impactor with a maximum deviation of ±5o.

6.1.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.1.3.1 Acceleration - time: The selection of the

specific acceleration - time recording equipment, in-

cluding transducers and recorders, is at the discretion

of the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the peak acceleration value to an accuracy of ±5% of

the true value. The total system, detection and re-

cording, shall be capable of measuring impact accel-

erations of up to 200 g at frequencies from 2 to

1000 Hz to an accuracy of ±5%. The minimum sam-

pling rate of the data acquisition system shall be

5000 Hz.

6.1.3.2 Displacement - time: It is optional, but de-

sirable, that the displacement - time history is re-

corded by a separate transducer. Any transducer that

provides a linear signal proportional to the displace-

ment of the impactor along the impact axis which can

be monitored simultaneously with the acceleration -

time trace is acceptable. If displacement is recorded,

the test equipment shall have means to determine and

record the top plane (base plane) of the test specimen

from which the total deformation and rebound height

are determined.

6.1.3.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

IV

MAG 2

01.12.1994

3

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

6.2 Test B - Top friction of the horse body:

6.2.1 Measurement device: Any type of friction

testing apparatus that is capable of pulling a slider on

the surface of a specimen horse body at a given load-

ing velocity is acceptable. During the test, the traction

force – time history of the slider shall be monitored

and recorded.

6.2.2 Slider: The slider shall have a mass of 5 kg ±

0.2 kg. A square-shaped test sole with a thickness of

10mm ± 0.5 mm and a size of 40 mm ± 1 mm shall be

bonded to the bottom of the slider. The thickness of

the test sole shall be decreased to 75% ± 5% of the

original thickness at a pressure of 5 N/cm2. The coef-

ficient of static friction of the test sole shall be

0.25 ± 0.03.

6.2.3 The slider shall be pulled at a constant load-

ing rate of 5 N/s ± 0.5 N/s.

6.2.4 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.2.4.1 Force - time: The selection of the specific

force - time recording equipment, including trans-

ducer and recorder, is at the discretion of the test

laboratory. The total system, detection and recording,

shall be capable of measuring traction forces up to

100 N at frequencies from 2 to 100 Hz to an accuracy

of ± 3%. The minimum sampling rate of the data ac-

quisition system shall be 200 Hz.

6.3 Test C - Positional stability of the pommels:

6.3.1 Measurement device: Any type of static test-

ing apparatus that is capable of stretching a pair of

pommels outward in the horizontal direction with a

given force, and monitors and records the static dis-

placement between the pommels is acceptable.

6.3.2 Static stretching force: The static stretching

force shall be 600 N ± 20 N, horizontally applied be-

tween the pommels.

6.3.3 Recording equipment for the static displace-

ment: The selection of the specific measurement

equipment is at the discretion of the test laboratory.

However, the accuracy of the measurement shall be

±0.1 mm.

6.4 Test D - Friction of the pommels:

6.4.1 Measurement device: Any type of friction

testing apparatus that is capable of measuring the

static friction force of a pommel is acceptable. A

pommel shall be set like a pulley with a testing belt

hung on it. One end of the testing belt shall be pulled

by the weight of 5 kg ±0.2 kg The traction force of

the other end shall be measured. See Figure 4 for an

illustration.

6.4.2 Testing belt: The width of the testing belt

FIG International Gymnastics Federation

Standard Specification for Pommel Horses

MAG – Men Artistic Gymnastics

shall be 20 mm ± 1 mm. The contacting side of the

testing belt shall have a layer with a thickness of

10 mm ± 0.5 mm. .The thickness of the layer shall be

decreased to 75% ± 5% of the original thickness at a

pressure of 5 N/cm2. The coefficient of static friction

of the layer shall be 0.25 ± 0.03.

6.4.3 Recording equipment for the static displace-

ment: The selection of the specific measurement

equipment is at the discretion of the test laboratory.

However, the system shall be capable of measuring

traction force up to 100 N to an accuracy of ±3%.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of a complete pommel horse as it is intended

to be used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG2.

8 Conditioning and Test Temperature

8.1 The test specimen shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 Test A – Shock absorption of the horse body:

9.1.1 Impact sites: A total of five impact sites shall

be designated on the test specimen. See Figure 1 for

an illustration of the impact sites.

Figure 1: Impact sites on the horse body (distances in

mm)

400

IV

MAG 2

01.12.1994

4

9.1.2.4 Upon completion of a given impact test,

raise the impactor off the surface of the test specimen.

9.1.2.5 The duration between tests at a given impact

site shall not be less than 120 seconds.

9.1.2.6 Each test specimen shall receive a total of

50 impacts. Impact each of the five impact sites ten

times.

9.1.3 Calculations:

9.1.3.1 Immediately following each test, record the

following measurements: Deflection (mm), Height of

rebound (mm) and Fmax (N).

9.1.3.2 The last eight tests for each impact site shall

be used to determine the arithmetic mean value of a

measured variable for each impact site and for the

overall mean value of a measured variable across all

impact sites.

9.2 Test B – Top friction of the horse body:

9.2.1 Test sites and directions: A total of three test

sites shall be designated on the test specimen as illus-

trated in Figure 2. Four orthogonal test directions for

the traction of the slider shall be also designated on

each test site as illustrated in Figure 2.

Figure 2: Top friction test sites and directions on the

horse body (distances in mm)

Longitudinal Direction

1

2

3

400

400

400

Lateral Direction

1

2

3

4

5

100

300

400

400

300

100

9.1.2 Impact test procedures:

9.1.2.1 Place the test specimen under the impact

test machine on a smooth, solid and horizontal floor

(concrete or metal plate) and orient the impactor such

that the centre of the impact face will contact one of

the designated impact test sites.

9.1.2.2 Raise the impactor to an appropriate drop

height such that it will contact the test specimen with

an impact velocity of 2.80 m/s ±3%. This corre-

sponds to a theoretical drop height of 0.4 m.

9.1.2.3 Release the impactor and capture the accel-

eration - time history and displacement - time history

(if applicable) using recording equipment described in

Section 6.1.3.

9.2.2 Friction test procedures:

9.2.2.1 Place the complete test specimen on a

smooth, solid and horizontal floor.

9.2.2.2 Put the slider on the pommel horse in such

a manner that the centre of its sole will contact one of

the designated test sites, and also in such a manner

that the pulling direction of the slider will conform to

one of the designated test directions. Immediately

prior to placing the slider, magnesium carbonate

powder of 1g shall be spread on the surface of the test

site. This shall be repeated prior to each test.

9.2.2.3 Pull the slider horizontally at a constant

loading rate of 5 N/s ± 0.5 N/s and capture the trac-

tion force – time history using the recording equip-

ment described in Section 6.2.4.

9.2.2.4 Repeat the procedure given in 9.2.2.2 and

9.2.2.3 five times at each test site and in each test di-

rection.

9.2.2.5 Each test specimen shall receive a total of

FIG International Gymnastics Federation

Standard Specification for Pommel Horses

MAG – Men Artistic Gymnastics

60 friction test procedures.

9.2.3 Calculations:

9.2.3.1 Immediately following each test, calculate

and record the friction coefficient.

9.2.3.2 Determine the overall mean value of the

friction coefficients across the test sites 1 to 3. De-

termine also the difference between the highest and

the lowest mean value of the friction coefficient be-

tween all test sites, and the difference between mean

values of the friction coefficients of orthogonal test

directions between all test sites.

9.3 Test C – Positional stability of the pommels:

9.3.1 Loading and measuring points: A total of

three pairs of loading points shall be designated on

the test specimen as illustrated in Figure 3. The dis-

placement shall be measured at these points.

Figure 3: Loading and measuring points of the pommels

(distances in mm)

IV

MAG 2

01.12.1994

5

measured variables for all loading points.

9.4 Test D – Friction of the pommels:

9.4.1 Friction test procedures:

9.4.1.1 Remove the specimen pommels from the

horse body and fasten each pommel to the testing po-

sition such that the testing belt shall be hung on at the

middle point of the specimen pommel.

9.4.1.2 Hang the testing belt on the pommel and

connect one end of the testing belt to a transducer that

can measure the traction force as illustrated in Fig-

ure 4. Immediately prior to hanging the testing belt,

magnesium carbonate powder of 1 g shall be spread

on the surface of the specimen pommel each time.

9.4.1.3 Pull the other end of the testing belt by the

weight of 5 kg ± 0.2 kg and measure the traction force

10 seconds after weighting.

1

2

3

85

Figure 4: Setup of friction test of the pommels

Pommel

Testing belt

9.3.2 Stretching test procedures:

9.3.2.1 Place the complete test specimen on a

smooth, solid and horizontal floor.

9.3.2.2 Set the loading device between the speci-

men pommels such that the loading axis will pass

through one of the pairs of the loading points illus-

trated in Figure 3.

9.3.2.3 Stretch the specimen pommels horizontally

up to the stretching force of 600 N ± 20 N and meas-

ure the incremental displacement between the speci-

men pommels using recording equipment described in

Section 6.3.3. Measurement shall be done within

10 seconds after reaching the prescribed stretching

force.

9.3.2.4 Measure the residual displacement between

the specimen pommels 60 seconds after the removal

of the stretching force.

9.3.2.5 Repeat the procedures given in 9.3.2.2,

9.3.2.3 and 9.3.2.4 at each of the specified loading

points.

9.3.3 Calculations:

9.3.3.1 Immediately following each test, record the

displacement of the pommels and the residual dis-

placement of the pommels.

9.3.3.2 Determine the overall mean values of the

：

1 2, 3,

Loading and measuring points

85

70

70

Load cell

Weight

5kg

9.4.1.4 Repeat the procedure given in 9.4.1.2 and

9.4.1.3 ten times for each pommel. Repeat the same

procedure in the opposite frictional direction. A pair

of specimen pommels shall receive a total of

40 friction test procedures.

9.4.2 Calculations:

9.4.2.1 Immediately following each test, record the

traction force. The frictional force of the pommel is

defined as the pulling weight minus the traction force.

Use this value to calculate the friction coefficient of

the pommel.

9.4.2.2 Determine the overall mean value of the

friction coefficient for both pommels. Determine also

the difference of the mean values of the friction coef-

ficients between the two pommels.

9.5 Calculate the values of all required variables

rounded to the decimal places of the corresponding

FIG International Gymnastics Federation

Standard Specification for Pommel Horses

MAG – Men Artistic Gymnastics

figures identified in Section 5.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested pommel

horse, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions under which the tests were made,

including test date, temperature and humidity.

10.1.5 Identification of performed parts of the test –

Test A, Test B, Test C and Test D.

10.1.6 Description of the impactor mass and the

drop height conditions (Test A), mass, loading rate of

the slider (Test B), static load (Test C) and the weight

of the testing belt (Test D).

10.1.7 Description of all test results related to the

IV

MAG 2

01.12.1994

6

performance requirements identified in Section 5.

10.1.8 Supplemental description of the test results:

10.1.8.1 Maximum value, minimum value and stan-

dard deviation of deflection, height of rebound and

Fmax variables according to Test A.

10.1.8.2 Mean values of deflection, height of re-

bound and Fmax for the last eight tests at each impact

site according to Test A.

10.1.8.3 Deflection, height of rebound and Fmax

values for all tests according to Test A.

10.1.8.4 Mean values and standard deviations of the

friction coefficient at each test site and direction ac-

cording to Test B.

10.1.8.5 Friction coefficient values for all tests ac-

cording to Test B.

10.1.8.6 Displacement of the pommels and residual

displacement of the pommels for all loading points

according to Test C.

10.1.8.7 Mean values and standard deviations of

friction coefficient of each pommel and frictional di-

rection according to Test D.

10.1.8.8 Friction coefficient values for all tests ac-

cording to Test D.

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

FIG International Gymnastics Federation

Standard Specification for Rings

MAG – Men Artistic Gymnastics

Standard Specification: Rings for Men Artistic Gymnastics

IV

MAG 3

1989

1

This standard is issued under the fixed designation FIG: IV-MAG3-1989; the numbers immediately following the

designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last revision.

This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test laboratories.

This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of rings and to

minimize any differences between competition and

training equipment.

1 Scope

1.1 This specification covers the inspection of sta-

bility for rings. This standard specification is applica-

ble to all ring frames that are to be used at any FIG-

sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a ring frame which

complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG3

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Static tractive force: The predetermined value

of force exerted on one ring while pulling the ring

vertically downwards.

3.1.2 Starting position: The vertical position of the

unloaded ring within the mounted ring frame before

loading it with a defined static tractive force. The

lower inner side of the ring shall serve as the point of

reference.

4 Principle of Measurement

4.1 The rings of a mounted ring frame are pulled

vertically downwards with a predetermined static trac-

tive force. After the release of the static tractive force

the rings must return into the starting position.

5 Performance Requirements

When tested according to the procedures described in

Section 9, the rings shall return into the starting posi-

tion within a tolerance of 5mm and no damage or re-

sidual deflection shall be observable.

6 Test Set-up and Apparatus

6.1 Any type of test set-up is acceptable that is ca-

pable to stress the test specimen under prescribed

conditions.

6.2 The device which applies the test load to the

ring shall have a width of 35mm ± 1mm.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of a complete ring frame as it is intended to be

used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG3.

8 Conditioning and Test Temperature

8.1 The ring frame, mounted and assembled for use,

shall be preconditioned at 50% ± 10% relative humid-

ity and 21° C ± 3° C for a minimum of 24 hours prior

to the test. All testing shall be carried out under the

same conditions.

9 Laboratory Procedure (Test Method)

9.1 Mount the ring frame with the rings at a height

as prescribed for competitions (Part II).

9.2 Install the traction device on one ring and de-

termine the starting position.

9.3 Pull the ring vertically downwards with a static

tractive force of 4000 N ± 40 N.

9.4 After the release of the static tractive force ver-

ify whether the ring returns into the starting position.

Report any fraction or observed permanent deflection

in any part of the test specimen.

9.5 Repeat the procedure given in 9.3 to 9.5 for the

other ring.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested ring

frame, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

FIG International Gymnastics Federation

Standard Specification for Rings

MAG – Men Artistic Gymnastics

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

IV

MAG 3

1989

2

perature and humidity.

10.1.5 Test height of the rings and cable tension of

the mounted and unloaded ring frame.

10.1.6 Description of the static tractive force.

10.1.7 Description whether fracture or other dam-

age has occurred or if any permanent deformation has

been observed after the test.

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

FIG International Gymnastics Federation

Standard Specification for Vaulting Tables

MAG – Men Artistic Gymnastics

IV

MAG 4

01.02.2001

1

Standard Specification: Vaulting Tables for Men Artistic Gymnastics

This standard is issued under the fixed designation FIG: IV-MAG4new-01.02.2001; the numbers immediately fol-

lowing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last

revision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test

laboratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of vaulting tables

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of

the profile dimensions, certain shock-absorbing char-

acteristics, the impact force - time relationships, and

the rebound properties of vaulting tables. This stan-

dard specification is applicable to all vaulting tables

that are to be used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a vaulting table which

complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG4new.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Starting position of an impact site: The verti-

cal position of an impact site at the surface of an

unloaded vaulting table from which the total deflec-

tion and total height of rebound is determined.

3.1.3 Deflection: The measured distance (in mm)

between the starting position of an impact site and the

maximum displacement of the impactor below the

starting position of an impact site.

3.1.4 Force (F): The product of the mass of the im-

pactor, expressed in kg, and the acceleration of the

impactor, expressed in m/s2.

3.1.5 Maximum Force (Fmax): The maximum value

of force measured during the impact and expressed in

Newtons.

3.1.6 Height of rebound: The measured distance (in

mm) between the starting position of an impact site

and the maximum displacement of the impactor above

the starting position of an impact site.

3.1.7 Impactor: The striking part of the test appara-

tus.

3.1.8 Impact velocity: The velocity of the impactor,

expressed in m/s, immediately prior to crossing the

starting position of an impact site on impact.

3.1.9 Theoretical drop height: A calculated drop

height which equates the measured velocity of the im-

pactor at the moment of impact to a height that would

generate the same velocity if the test were performed

at sea level and there was no friction to retard the im-

pactor during a drop from that height.

4 Principle of Measurement

4.1 A test specimen is impacted at a specified ve-

locity with an impactor of given mass and geometry.

A transducer mounted in the impactor monitors the

acceleration – time history of the impactor which is

recorded with the aid of a data acquisition system. An

additional transducer may be used to monitor the dis-

placement – time history of the impactor.

4.2 Dynamic data obtained during these procedures

are indicative of the cushioning and rebound proper-

ties of vaulting tables used in training and FIG-

sanctioned competitions.

5 Performance Requirements

5.1 When tested according to the procedures de-

scribed in Section 9, the overall mean values and

maximum ranges of the measured variables across all

impact sites shall be within the figures of Table 1.

FIG International Gymnastics Federation

Standard Specification for Vaulting Tables

MAG – Men Artistic Gymnastics

Table 1: Figures for Vaulting Tables

x represents the mean value of the measured variable

IV

MAG 4

01.02.2001

2

Deflection

(mm)

Mean

value

Max.

range

Height of re-

bound (mm)

Fmax

(N)

x ≤2500

≤550

34 ≤x ≤44 120 ≤x ≤180

≤10

≤75

6 Test Apparatus

6.1 Profile dimension test device: The selection of

the specific profile dimension test device, including

transducers and recorders, is at the discretion of the

test laboratory. However, the recording system shall

be capable of measuring profile dimensions at spe-

cific measurement points orthogonal to the given

standard profile line to an accuracy of ±0.5 mm. The

total system, detection and recording, shall be capable

of measuring proportional profile dimensions at spe-

cific measurement lines (see Section 9.1).

6.2 Impact test machine: Any type of dynamic test-

ing apparatus that is capable of impacting a test

specimen at a prescribed impact velocity monitoring

and recording the acceleration - time history of the

impactor is acceptable. The impact test machine and

the impactor shall have sufficient rigidity to eliminate

undesirable vibrations in the apparatus which might

be recorded on the acceleration - time curve. The im-

pact test machine shall also be designed in such a

manner that only the impact face contacts the test

specimen at any time during the test procedures.

6.3 Impactor: The impactor shall be 10 kg ±0.1 kg

and shall have a flat impact face with a

10 cm ±0.5 cm diameter. The edge of the impactor

face should be relieved to eliminate sharp edges. Pro-

vision shall be made so that the accelerometer can be

securely fastened parallel to the vertical axis of the

impactor with a maximum deviation of ±5o.

6.4 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.4.1 Acceleration - time: The selection of the spe-

cific acceleration - time recording equipment, includ-

ing transducers and recorders, is at the discretion of

the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the peak acceleration value to an accuracy of ±5% of

the true value. The total system, detection and re-

cording, shall be capable of measuring impact accel-

erations of up to 200 g at frequencies from 2 to

1000 Hz to an accuracy of ±5%. The minimum sam-

pling rate of the data acquisition system shall be 5000

Hz.

6.4.2 Displacement - time: It is optional, but desir-

able, that the displacement - time history is recorded

by a separate transducer. Any transducer that provides

a linear signal proportional to the displacement of the

impactor along the impact axis which can be moni-

tored simultaneously with the acceleration - time trace

is acceptable. If displacement is recorded, the test

equipment shall have means to determine and record

the starting position of an impact site from which the

total deformation and rebound height are determined.

6.4.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of a complete vaulting table as it is intended to

be used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG4new.

7.3 The profile dimensions of the test specimen

shall be inspected according to the procedures de-

scribed in Section 9.1.

8 Conditioning and Test Temperature

8.1 Test specimens shall be preconditioned at 50%

±10% relative humidity and 21o C ±3o C for a mini-

mum of 24 hours prior to the test. All testing shall be

carried out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 Profile dimension measurement:

9.1.1 Measurement locations: A total of 42 meas-

urement points (MP) on five measurement lines are

used to inspect the profile dimensions. In longitudinal

direction there are 14 measurement points on the cen-

ter measurement line of the test specimen (MP1 and

MP16 are not required for standardization). In trans-

versal direction there are 28 measurement points,

seven at each measurement line (four transversal

lines, orthogonal crossing the center measurement line

at MP4, MP5, MP7 and MP9). See Figures 1-3 for

illustrations of the measurement points.

9.1.2 Profile dimension measurement procedures:

9.1.2.1 Place the test specimen under the profile

dimension test device on a horizontal, smooth and

solid floor.

9.1.2.2 Determine the proportional profile dimen-

sions for each measurement line (four transversal pro-

files and one longitudinal profile).

9.1.3 Determination of the orthogonal deviations to

FIG International Gymnastics Federation

Standard Specification for Vaulting Tables

MAG – Men Artistic Gymnastics

the standard profile (in orientation of the designated

arrows in Figures 1 and 3):

9.1.3.1 Longitudinal direction: Compare the actual

profile to the standard profile by crossing (overlaying)

the profiles in MP5 and MP14 (i.e. the deviation in

these measurement points is set to zero by shifting the

profiles in horizontal and vertical direction without

rotation). Calculate the deviations at the remaining

measurement points.

9.1.3.2 Transversal direction: Compare the actual

profile to the standard profile for each transversal

measurement line by crossing (overlaying) the pro-

files in the center measurement point N4 (i.e. the de-

viation in this measurement points is set to zero by

shifting the profiles in horizontal and vertical direc-

tion without rotation). Calculate the deviations at the

remaining measurement points.

Figure 1: Dimension Measurement Locations for Vault-

ing Tables – Measurement Points on Center Line in

Longitudinal Direction (MP1 – MP16)

(Side view - distances in cm)

IV

MAG 4

01.02.2001

3

Figure 2: Dimension Measurement Locations for Vault-

ing Tables – Measurement Lines in Transversal Direc-

tion (Line MP4 / MP5 / MP7 / MP9)

(Frontal view - distances in cm)

Figure 3: Dimension Measurement Locations for Vault-

ing Tables – Measurement Points on Measurement Lines

in Transversal Direction (N1 – N7)

(Transverse section)

9.2 Impact locations: A total of eleven impact sites

shall be designated on the test specimen. See Figure 4

for an illustration of the impact sites.

FIG International Gymnastics Federation

Standard Specification for Vaulting Tables

MAG – Men Artistic Gymnastics

Figure 4: Impact Locations for Vaulting Tables

(Oversight view - distances in mm)

IV

MAG 4

01.02.2001

4

Figure 7: Impact Test Setup for Test Points 7 – 11

9.3 Impact test procedures:

9.3.1 Place and tilt the test specimen under the im-

pact test machine such that the centre of the impact

face of the impactor will contact one of the designated

impact test sites perpendicular to the surface of the

vaulting table. See Figures 5-7 for illustrations of the

tilted test positions. It is optional, but desirable, to en-

able the necessary tilt angles of the test specimen by

attaching the test specimen to a smooth, solid metal

plate with the same inclination.

Figure 5: Impact Test Setup for Test Points 1,2,3

Figure 6: Impact Test Setup for Test Points 4,5,6

9.3.2 Raise the impactor to an appropriate drop

height such that it will contact the test specimen with

an impact velocity of 2.80 m/s ±3 %. This corre-

sponds to a theoretical drop height of 0.4 m.

9.3.3 Release the impactor and capture the accel-

eration - time history and displacement - time history

(if applicable) using recording equipment described in

Section 6.4.

9.3.4 Upon completion of a given impact test, raise

the impactor off the surface of the test specimen.

9.3.5 The duration between tests at a given impact

site shall not be less than 120 seconds.

9.3.6 Each test specimen shall receive a total of 110

impacts. Impact each of the eleven impact sites ten

times.

9.4 Calculations:

9.4.1 Immediately following each test, record the

following measurements: Fmax (N), Deflection (mm)

and Height of rebound (mm).

9.4.2 The last eight tests for each impact site shall

be used to determine the arithmetic mean value of a

FIG International Gymnastics Federation

Standard Specification for Vaulting Tables

MAG – Men Artistic Gymnastics

measured variable for each impact site and for the

overall mean value of a measured variable across all

impact sites.

9.4.3 Calculate the mean values of Deflection,

Height of rebound and Fmax across all impact sites

rounded to zero decimal places.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested vaulting

table, including type, source, manufacturer’s appara-

tus denomination, manufacturer’s model number (if

appropriate), dimensions of test specimen, and any

other pertinent information. Photographs may be in-

cluded in the test report for sample documentation

purposes.

10.1.2 Description of the profile dimensions rela-

tive to the requirements in FIG Apparatus Rules: II-

MAG4new.

10.1.3 Test identification number according to the

IV

MAG 4

01.02.2001

5

internal regulations between the FIG Test Institutes.

10.1.4 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.5 Conditions of test, including test date, tem-

perature and humidity.

10.1.6 Description of the impactor mass and the

drop height conditions.

10.1.7 Description of the test results relative to the

performance requirements identified in Section 5.

10.1.8 Mean values of Deflection, Height of re-

bound and Fmax across all impact sites.

10.1.9 Maximum value, minimum value and stan-

dard deviation of Deflection, Height of rebound and

Fmax variables.

10.1.10 Mean values of Deflection, Height of re-

bound and Fmax for the last eight tests at each impact

site.

10.1.11 Deflection, Height of rebound and Fmax val-

ues for all tests.

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

6

FIG International Gymnastics Federation

Standard Specification for Parallel Bars

MAG – Men Artistic Gymnastics

Standard Specification: Parallel Bars for Men Artistic Gymnastics

IV

MAG 5

01.01.1997

1

This standard is issued under the fixed designation FIG: IV-MAG5-01.01.1997; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of parallel bars

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain static stiffness properties, dynamic force - time

and displacement - time relationships as well as oscil-

lation and stability characteristics of parallel bars.

This standard specification is applicable to all parallel

bars that are to be used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using parallel bars which

comply with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG5.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: IV-MAG6.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Bar linkage: A rigid mechanical linkage be-

tween both bars of a parallel bars to exert equal forces

simultaneously on both bars.

3.1.2 Static tractive force: The predetermined value

of force (in N) exerted on the midpoint of the bar,

pulling the bar vertically downwards.

3.1.3 Starting position: The position of an unloaded

bar or an unloaded bar linkage from which the total

deflection in vertical direction is determined. The

midpoint of the bar or the bar linkage shall serve as

the point of reference for the measurements.

3.1.4 Deflection: The measured distance (in mm)

between the starting position and the maximum dis-

placement of the midpoint of the bar or the bar link-

age in vertical direction.

3.1.5 Definition of spatial dimensions and test di-

rections: For the determination of the vertical deflec-

tion of the midpoint of the bar or the bar linkage the

spatial dimensions are defined as illustrated in Figure

1 to 3. The test directions are defined as illustrated in

Figure 4.

3.1.6 Pendulum: Tubular test body of given dimen-

sions and mass with an additional low-friction falling

weight inside. The test body is attached to a bar or a

bar linkage with the help of two inflexible grasping

arms, each of which is at the same distance from the

midpoint of the bar or the bar linkage, guaranteeing a

low-friction rotation of the test body about the longi-

tudinal axis of the bar or the bar linkage.

Figure 1: Definition of Spatial Dimensions

Test position: Middle of bars (lateral)

(Pendulum in horizontal position before release)

Figure 2: Definition of Spatial Dimensions

Test position: Middle of bars (transversal)

(Pendulum in horizontal position before release)

FIG International Gymnastics Federation

Standard Specification for Parallel Bars

MAG – Men Artistic Gymnastics

Figure 3: Definition of Spatial Dimensions

Test position: End of bars (transversal)

(Pendulum in horizontal position before release)

IV

MAG 5

01.01.1997

2

tion.

3.1.14 Maximum amplitude: Value of the amplitude

(in mm) of the first oscillation of the bar-pendulum

system after the release of the initial tension.

3.1.15 Half amplitude: Value of the amplitude

(in mm) of the first oscillation which is equal to or

less than half the maximum amplitude.

3.1.16 Half amplitude interval: Duration of oscilla-

tion (in ms) between the passage of the maximum

amplitude and the reaching of the half amplitude. See

Figure 5 for illustration.

Figure 5: Oscillation Damping Parameters

Figure 4: Definition of Test Directions

3.1.7 Maximum Force (Fmax): The maximum value

of the reaction force in the direction of the pendulum's

centre of gravity measured as the sum of the forces

exerted on both grasping arms during the pendulum

swing, expressed in Newtons.

3.1.8 Hanging position: Stable equilibrium position

of the hanging pendulum under gravity conditions

only.

3.1.9 Horizontal position: Position of the attached

pendulum rectangular to the hanging position.

3.1.10 Additional falling weight: Cylindrical test

body of given dimensions and mass inside the pendu-

lum producing an additional impact stress on the

gymnastic apparatus during pendulum swing.

3.1.11 Internal drop height: Predetermined sliding

distance of the additional falling weight inside the

pendulum.

3.1.12 Initial tension: Predetermined value of the

force (in N) exerted on the bar or the bar linkage,

composed of the gravity of the attached pendulum and

an additional tractive force pulling the bar-pendulum

system vertically downwards.

3.1.13 Frequency of oscillation: Reciprocal of the

value determined by the duration of the half ampli-

tude interval divided by the number of oscillations of

the bar-pendulum system within the half amplitude

interval. The frequency is expressed in Hertz. See

Figure 5 for illustration of the frequency determina-

4 Principle of Measurement

4.1 The complete measurement is composed of four

specific test procedures:

4.1.1 Test A - Static traction stress: A bar of a

mounted apparatus is pulled vertically downwards

with a predetermined static tractive force. A measur-

ing device mounted on the bar monitors the displace-

ment - time history of the midpoint of the bar caused

by this force. The maximum deflection is recorded

with the aid of a data acquisition system. After the

release of the static tractive force the bar must return

into the starting position.

4.1.2 Test B - Stress by pendulum swing: A pendu-

lum which is attached to a bar or a bar linkage of a

mounted apparatus is rotated from hanging position

into horizontal position and then released. While it

swings down, an additional falling weight inside the

tubular pendulum slides down from a predetermined

internal drop height until the weight strikes against the

inside bottom of the pendulum, producing an addi-

tional impact stress on the gymnastic apparatus. A

measuring device monitors the displacement - time

history of the midpoint of the bar or the bar linkage.

Load cells inside both pendulum grasping arms moni-

FIG International Gymnastics Federation

Standard Specification for Parallel Bars

MAG – Men Artistic Gymnastics

tor the reaction force - time history of the pendulum.

Both are recorded with the aid of a data acquisition

system. The test measures the maximum reaction

force in the direction of the pendulum's centre of

gravity and the positive deflection of the bar or the

bar linkage in vertical direction.

4.1.3 Test C - Oscillation damping: A pendulum

which is attached to a bar or a bar linkage of a

mounted apparatus is pulled vertically downwards un-

til a predetermined initial tension is reached. The

abrupt release causes a damped oscillation of the bar-

pendulum system. A measuring device monitors the

displacement - time history of the midpoint of the bar

or the bar linkage which is recorded with the aid of a

data acquisition system. The test measures the fre-

quency as well as the half amplitude interval of the

oscillation.

4.1.4 Test D - Lateral stability: One bar of a paral-

lel bars which is ensured against sideward slipping is

pulled horizontally in lateral direction until a prede-

termined inclination of the parallel bars is reached. A

load cell inside the towing cable monitors the tractive

force - time history which is recorded with the aid of a

data acquisition system. The test measures the tractive

force in the predetermined inclination position of the

parallel bars.

4.2 Static and dynamic data obtained during these

procedures are indicative of the static stiffness, elas-

tic, damping, oscillation and stability properties of

parallel bars used in training and FIG-sanctioned

competitions.

5 Performance Requirements

5.1 Test A - Static traction stress: When tested ac-

cording to the procedures described in Section 9.2,

the value of the measured variable shall be within the

figures of Table 1.

Table 1: Figure for Test A – Static traction stress

x represents the measured variable

Test A: Static traction stress

Deflection (mm)

50 ≤x ≤70

IV

MAG 5

01.01.1997

3

Table 2: Figures for Test B – Stress by pendulum swing

x represents the mean value of the measured variable

Test B: Stress by pendulum swing

Middle of bars (lateral)

Fmax (N)

Positive vertical deflection (mm)

Middle of bars (transversal)

Fmax (N)

Positive vertical deflection (mm)

End of bars (transversal)

Fmax (N)

Positive vertical deflection (mm)

x ≤3000

63 ≤x ≤73

x ≤2750

62 ≤x ≤77

x ≤2300

85 ≤x ≤115

5.3 Test C - Oscillation damping: When tested ac-

cording to the procedures described in Section 9.4,

the mean values of the measured variables shall be

within the figures of Table 3.

Table 3: Figures for Test C – Oscillation damping

x represents the mean value of the measured variable

Test C: Oscillation damping

Middle of bars (lateral)

Frequency of oscillation (Hz)

Half amplitude interval (ms)

Middle of bars (transversal)

Frequency of oscillation (Hz)

Half amplitude interval (ms)

End of bars (transversal)

Frequency of oscillation (Hz)

Half amplitude interval (ms)

3.80 ≤x ≤5.00

400 ≤x ≤1200

4.00 ≤x ≤4.80

400 ≤x ≤2500

3.00 ≤x ≤3.60

400 ≤x ≤2750

5.4 Test D - Lateral stability: When tested accord-

ing to the procedures described in Section 9.5., the

value of the measured variable shall be within the fig-

ure of Table 4. If the parallel bars do not meet this

requirement the manufacturer and the appropriate FIG

authorities will be informed that at all FIG sanctioned

competitions and events, the parallel bars must be

fixed to the floor.

Table 4: Figure for Test D – Lateral Stability

x represents the measured variable

Test D: Lateral stability

Tractive force (N)

x ≥900

5.2 Test B - Stress by pendulum swing: When tested

according to the procedures described in Section 9.3,

the mean values of the measured variables shall be

within the figures of Table 2.

6 Test Set-up and Apparatus

6.1 Set-up for Test A - Static traction stress: Any

type of test set-up is acceptable that is capable to

stress the test specimen under prescribed conditions

FIG International Gymnastics Federation

Standard Specification for Parallel Bars

MAG – Men Artistic Gymnastics

and monitoring and recording the displacement - time

history of the midpoint of the bar.

6.2 Set-up for Test B - Stress by pendulum swing:

Any type of test set-up is acceptable that is capable of

stressing the test specimen with a pendulum swing

under prescribed conditions and monitoring and re-

cording the displacement - time history of the mid-

point of the bar or the bar linkage and the reaction

force - time history of the pendulum. It is optional,

but desirable, that the pendulum is released from a

magnet in the horizontal position.

6.3 Set-up for Test C - Oscillation damping: Any

type of test set-up is acceptable that is capable of

stressing a bar-pendulum system under prescribed

conditions and monitoring and recording the dis-

placement - time history of the midpoint of the bar or

the bar linkage. It is optional, but desirable, that the

bar-pendulum system is released from a magnet at the

prescribed initial tension.

6.4 Set-up for Test D - Lateral stability: Any type

of test set-up is acceptable that is capable to stress the

test specimen under prescribed conditions and moni-

toring and recording the tractive force - time history

of the towing cable.

6.5 Bar linkage: Any type of rigid mechanical link-

age between the bars is acceptable which enables an

attachment of the pendulum for all tests in transversal

test direction. The bar linkage shall enable a distance

between the bars of 52 cm ± 1 cm. The weight of the

bar linkage shall be 3.0 kg ± 0.3 kg.

6.6 Pendulum - The pendulum shall meet the fol-

lowing criteria:

6.6.1 Mass and geometry: The tubular test body

shall have a mass of 40.0 kg ± 3% (including load

cells, grasping arms and appliances for additional

weights) and a geometry as specified in Figure 6. The

load cells shall be located between the test body and

the grasping arms. The weight of each grasping arm

shall be 1.0 kg ± 3%.

6.6.2 Pendulum fixation - The pendulum fixation to

the bar shall meet the following criteria:

6.6.2.1 Functional properties: The fixation shall al-

low an immediate transfer of forces between pendu-

lum and bar or bar linkage and guarantee a low-

friction rotation of the pendulum about the longitudi-

nal axis of a bar or a bar linkage (the use of roll bear-

ings is recommended).

6.6.2.2 Friction of the bar-pendulum fixation - The

frictional properties of the fixation shall meet the cri-

teria as specified in FIG Apparatus Rules: IV-MAG6

Standard Specification for Horizontal Bars for Men

Artistic Gymnastics.

IV

MAG 5

01.01.1997

4

Figure 6: Geometry of Tubular Test Body

(All dimensions with an accuracy of 3%)

6.6.3 Additional falling weight - The additional fal-

ling weight shall meet the following criteria:

6.6.3.1 Mass and geometry: The cylindrical falling

weight shall have a mass of 20.0 kg ± 0.2 kg and a

geometry as specified in Figure 7.

Figure 7: Geometry of Additional Falling Load

(All dimensions with an accuracy of 3%)

6.6.3.2 Friction within the tube of the test body -

The frictional properties of the additional falling

weight shall meet the criteria as specified in FIG Ap-

paratus Rules: IV-MAG6 Standard Specification for

FIG International Gymnastics Federation

Standard Specification for Parallel Bars

MAG – Men Artistic Gymnastics

Horizontal Bars for Men Artistic Gymnastics.

6.6.3.3 Damping of the additional falling weight at

the inside bottom of the tubular test body: The damp-

ing properties of the additional falling weight shall

meet the criteria as specified in FIG Apparatus Rules:

IV-MAG6 Standard Specification for Horizontal Bars

for Men Artistic Gymnastics.

6.7 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.7.1 Displacement - time: The selection of the

specific displacement - time recording equipment, in-

cluding transducers and recorders, is at the discretion

of the test laboratory. However, the transducers shall

provide linear signals proportional to the displace-

ment of the midpoint of the bar or the bar linkage. If

displacement is recorded, the test equipment shall

have means to determine and record the starting posi-

tion of the bar or the bar linkage from which the total

deflection is determined. The total system, detection

and recording, shall be capable of measuring dis-

placements of up to 200 mm at frequencies from 2 to

200 Hz to an accuracy of ± 1%. The minimum sam-

pling rate of the data acquisition system shall be

500 Hz.

6.7.2 Reaction force - time: Any reaction force -

time recording equipment, including load cells and

recorders, which can monitor the reaction force ex-

erted on the pendulum simultaneously with the dis-

placement - time trace is acceptable. The total system,

detection and recording, shall be capable of measur-

ing reaction forces of up to 5000 N at frequencies

from 2 to 200 Hz to an accuracy of ± 1%. The mini-

mum sampling rate of the data acquisition system

shall be 500 Hz.

6.7.3 Tractive force: Any tractive force recording

equipment, including load cells and recorders, which

can monitor the tractive force exerted on the parallel

bars is acceptable. The total system, detection and re-

cording, shall be capable of measuring tractive forces

of up to 5000 N to an accuracy of ± 1%.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of complete parallel bars as it is intended to be

used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG5.

8 Conditioning and Test Temperature

8.1 The parallel bars, mounted and assembled for

use, shall be preconditioned at 50% ± 10% relative

humidity and 21° C ± 3° C for a minimum of 24 hours

prior to the test. All testing shall be carried out under

the same conditions.

IV

MAG 5

01.01.1997

5

9 Laboratory Procedure (Test Method)

9.1 General set-up:

9.1.1 Mount the parallel bars to a height as pre-

scribed for competitions (Part II).

9.1.2 For Test A, B and C the parallel bars shall

have a fixation to the floor to eliminate undesirable

vibrations and movements of the apparatus.

9.2 Test A - Static traction stress:

9.2.1 Install the displacement measuring device on

an unloaded bar and determine the starting position.

9.2.2 Pull the midpoint of one bar vertically down-

wards with a static tractive force of 1350 N ± 20 N

and capture, then record the resulting maximum de-

flection (mm) using recording equipment described in

Section 6.7.

9.2.3 After the release of the static tractive force

verify whether the bar returns into the starting posi-

tion.

9.3 Test B - Stress by pendulum swing:

9.3.1 Install the displacement measuring device on

an unloaded bar (tests in lateral test direction) or the

unloaded bar linkage (tests in transversal test direc-

tion) and determine the starting position.

9.3.2 Attach the pendulum (60 kg: 40 kg pendulum

with additional 20 kg falling weight) to a bar or the

bar linkage in hanging position.

9.3.3 Move the pendulum from hanging position

into horizontal position and move the additional fal-

ling weight inside the pendulum to the 50 cm ± 1 cm

internal drop height position. For the direction of the

pendulum swing at the different test positions see

Figure 1 to 3.

9.3.4 Release the pendulum and capture the dis-

placement - time history of the midpoint of the bar or

the bar linkage and the reaction force - time history of

the pendulum, using recording equipment described

in Section 6.7.

9.3.5 The parallel bars shall be stressed at each of

the following test positions by repeating the pendulum

swing five times: End of bars (transversal), Middle of

bars (transversal), Middle of bars (lateral). See Figure

1 to 4 for illustration of the locations and the direc-

tions of the test positions.

9.3.6 Immediately following each test, record the

following measurements: Fmax (N) and positive verti-

cal deflection (mm).

9.3.7 All five tests per test position shall be used to

determine the arithmetic mean values of the measured

variables.

9.4 Test C - Oscillation damping:

9.4.1 Attach the pendulum (60 kg: 40 kg pendulum

with additional 20 kg falling weight at the inside bot-

tom of the pendulum) to a bar (tests in lateral test di-

FIG International Gymnastics Federation

Standard Specification for Parallel Bars

MAG – Men Artistic Gymnastics

rection) or the bar linkage (tests in transversal test di-

rection) in hanging position.

9.4.2 Pull down the pendulum vertically until the

initial tension of 1000 N ± 30 N is reached.

9.4.3 Release the pendulum and capture the dis-

placement - time history of the midpoint of the bar or

the bar linkage using recording equipment described

in Section 6.7.

9.4.4 Repeat the above process for each test posi-

tion (see 9.3.5) five times.

9.4.5 Immediately following each test, record the

following measurements: Frequency (Hz) and half

amplitude interval (ms) of the oscillation.

9.4.6 All five tests per test position shall be used to

determine the arithmetic mean values of the measured

variables.

9.5 Test D - Lateral stability:

9.5.1 Ensure the parallel bars against sideward slip-

ping with a barrier at the base frame.

9.5.2 Mount the towing cables to one bar at the top

of the uprights and pull horizontally in lateral direc-

tion until the test specimen tilts to an inclination of

10°. Capture, then record the tractive force (N) using

recording equipment described in Section 6.7.

9.6 Calculate the values of all required variables

rounded to the decimal places of the corresponding

figures identified in Section 5.

10 Report

10.1 The test report shall include the following in-

IV

MAG 5

01.01.1997

6

formation:

10.1.1 Complete identification of the tested parallel

bars, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Test height of the parallel bars.

10.1.6 Test A - Static traction stress: Description of

the static tractive force.

10.1.7 Test B - Stress by pendulum swing: Descrip-

tion of the pendulum mass, the additional falling

weight and the internal drop height.

10.1.8 Test C - Oscillation damping: Description of

the pendulum mass (including the additional falling

weight at the inside bottom of the pendulum) and the

initial tension.

10.1.9 Test D - Lateral stability: Description of the

inclination of the parallel bars.

10.1.10 Description of the test results relative to the

performance requirements identified in Section 5.

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

FIG International Gymnastics Federation

Standard Specification for Horizontal Bars

MAG – Men Artistic Gymnastics

IV

MAG 6

29.03.1996

1

Standard Specification: Horizontal Bars for Men Artistic Gymnastics

This standard is issued under the fixed designation FIG: IV-MAG6-29.03.1996; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of horizontal bars

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain static stiffness properties, dynamic force - time

and displacement - time relationships and the oscilla-

tion characteristics of horizontal bars. This standard

specification is applicable to all horizontal bars that

are to be used at any FIG-sanctioned event.

1.2 The test procedures associated with this specifi-

cation does not imply that an injury cannot be in-

curred while using a horizontal bar which complies

with this specification.

1.3 This standard may involve hazardous operations

and equipment. This standard does not purport to ad-

dress all the safety problems associated with its use. It

is the responsibility of the user of this standard to es-

tablish appropriate safety and health practices and to

determine the applicability of regulatory limitations

prior to use.

2 Normative References

2.1 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG6.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Cable tension: The predetermined value of

force (in N) exerted on the mounting cables of the

completely-mounted unloaded horizontal bar.

3.1.2 Static tractive force: The predetermined value

of force (in N) exerted on the midpoint of the bar,

pulling the bar vertically downwards.

3.1.3 Starting position: The position of the

unloaded bar from which the total deflection in verti-

cal and horizontal direction is determined. The mid-

point of the bar shall serve as the point of reference

for the measurements.

3.1.4 Deflection: The measured distance (in mm)

between the starting position and the maximum dis-

placement of the midpoint of the bar in vertical and

horizontal direction respectively.

3.1.5 Definition of spatial dimensions: For the de-

termination of the vertical and horizontal deflection of

the midpoint of the bar the spatial dimensions are de-

fined as illustrated in Figure 1.

Figure 1: Definition of Spatial Dimensions

(Pendulum in horizontal position before release)

3.1.6 Pendulum: Tubular test body of given dimen-

sions and mass with an additional low-friction falling

weight inside. The test body is attached to the bar

with the help of two inflexible grasping arms, each of

which is at the same distance from the midpoint of the

bar, guaranteeing a low-friction rotation of the test

body about the longitudinal axis of the bar.

3.1.7 Maximum Force (Fmax): The maximum value

of the reaction force in the direction of the pendulum's

centre of gravity measured as the sum of the forces

exerted on both grasping arms during the pendulum

swing, expressed in Newtons.

3.1.8 Hanging position: Stable equilibrium position

of the hanging pendulum under gravity conditions

only.

3.1.9 Horizontal position: Position of the attached

pendulum rectangular to the hanging position.

3.1.10 Additional falling weight: Cylindrical test

body of given dimensions and mass inside the pendu-

lum producing an additional impact stress on the

gymnastic apparatus during pendulum swing.

3.1.11 Internal drop height: Predetermined sliding

distance of the additional falling weight inside the

pendulum.

3.1.12 Initial tension: Predetermined value of the

force exerted on the bar, composed of the gravity of

the attached pendulum and an additional tractive force

FIG International Gymnastics Federation

Standard Specification for Horizontal Bars

MAG – Men Artistic Gymnastics

pulling the bar-pendulum system vertically down-

wards.

3.1.13 Frequency of oscillation: Reciprocal of the

value determined by the duration of the half ampli-

tude interval divided by the number of oscillations of

the bar-pendulum system within the half amplitude

interval. The frequency is expressed in Hertz. See

Figure 2 for illustration of the frequency determina-

tion.

3.1.14 Maximum amplitude: Value of the amplitude

(in mm) of the first oscillation of the bar-pendulum

system after the release of the initial tension.

3.1.15 Half amplitude: Value of the amplitude

(in mm) of the first oscillation which is equal to or

less than half the maximum amplitude.

3.1.16 Half amplitude interval: Duration of oscilla-

tion (in ms) between the passage of the maximum

amplitude and the reaching of the half amplitude. See

Figure 2 for illustration.

Figure 2: Oscillation Damping Parameters

IV

MAG 6

29.03.1996

2

additional falling weight inside the tubular pendulum

slides down from a predetermined internal drop

height until the weight strikes against the inside bot-

tom of the pendulum, producing an additional impact

stress on the gymnastic apparatus. A measuring de-

vice monitors the two-dimensional displacement -

time history of the midpoint of the bar. Load cells in-

side both pendulum grasping arms monitor the reac-

tion force - time history of the pendulum. Both are

recorded with the aid of a data acquisition system.

The test measures the maximum reaction force in the

direction of the pendulum's centre of gravity as well

as the positive deflection of the bar in vertical direc-

tion and the positive and negative deflection of the

bar in horizontal direction.

4.1.3 Test C - Oscillation damping: A pendulum

which is attached to the bar of a mounted apparatus is

pulled vertically downwards until a predetermined

initial tension is reached. The abrupt release causes a

damped oscillation of the bar-pendulum system. A

measuring device monitors the displacement - time

history of the midpoint of the bar which is recorded

with the aid of a data acquisition system. The test

measures the frequency as well as the half amplitude

interval of the oscillation.

4.2 Static and dynamic data obtained during these

procedures are indicative of the static stiffness, elas-

tic, damping, and oscillation properties of the hori-

zontal bar used in training and FIG-sanctioned com-

petitions.

5 Performance Requirements

5.1 Test A - Static traction stress: When tested ac-

cording to the procedures described in Section 9.2,

the value of the measured variable shall be within the

figures of Table 1.

Table 1: Figure for Test A – Static traction stress

x represents the measured variable

Test A: Static traction stress

Deflection (mm)

80 ≤x ≤100

4 Principle of Measurement

4.1 The complete measurement is composed of

three specific test procedures:

4.1.1 Test A - Static traction stress: The bar of a

mounted apparatus is pulled vertically downwards

with a predetermined static tractive force. A measur-

ing device mounted on the bar monitors the displace-

ment - time history of the midpoint of the bar caused

by this force. The maximum deflection is recorded

with the aid of a data acquisition system. After the

release of the static tractive force the bar must return

into the starting position.

4.1.2 Test B - Stress by pendulum swing: A pendu-

lum which is attached to the bar of a mounted appara-

tus is rotated from hanging position into horizontal

position and then released. While it swings down, an

5.2 Test B - Stress by pendulum swing: When tested

according to the procedures described in Section 9.3,

the mean values of the measured variables shall be

within the figures of Table 2.

FIG International Gymnastics Federation

Standard Specification for Horizontal Bars

MAG – Men Artistic Gymnastics

Table 2: Figures for Test B – Stress by pendulum swing

x represents the mean value of the measured variable

Test B: Stress by pendulum swing

Fmax (N)

Positive vertical deflection (mm)

Negative horizontal deflection (mm)

Positive horizontal deflection (mm)

x ≤3200

120 ≤x ≤135

-30 ≤x ≤-40

60 ≤x ≤75

IV

MAG 6

29.03.1996

3

Figure 3: Geometry of Tubular Test Body

(All dimensions with an accuracy of 3%)

5.3 Test C - Oscillation damping: When tested ac-

cording to the procedures described in Section 9.4,

the mean values of the measured variables shall be

within the figures of Table 3.

Table 3: Figures for Test C – Oscillation damping

x represents the mean value of the measured variable

Test C: Oscillation damping

Frequency of oscillation (Hz)

Half amplitude interval (ms)

3.00 ≤x ≤3.25

1250 ≤x ≤4900

6 Test Set-up and Apparatus

6.1 Set-up for Test A - Static traction stress: Any

type of test set-up is acceptable that is capable to

stress the test specimen under prescribed conditions

and monitoring and recording the displacement - time

history of the midpoint of the bar.

6.2 Set-up for Test B - Stress by pendulum swing:

Any type of test set-up is acceptable that is capable of

stressing the test specimen with a pendulum swing

under prescribed conditions and monitoring and re-

cording the displacement - time history of the mid-

point of the bar and the reaction force - time history

of the pendulum. It is optional, but desirable, that the

pendulum is released from a magnet in the horizontal

position.

6.3 Set-up for Test C - Oscillation damping: Any

type of test set-up is acceptable that is capable of

stressing the bar-pendulum system under prescribed

conditions and monitoring and recording the dis-

placement - time history of the midpoint of the bar. It

is optional, but desirable, that the bar-pendulum sys-

tem is released from a magnet at the prescribed initial

tension.

6.4 Pendulum - The pendulum shall meet the fol-

lowing criteria:

6.4.1 Mass and geometry: The tubular test body

shall have a mass of 40.0 kg ± 3% (including load

cells, grasping arms and appliances for additional

weights) and a geometry as specified in Figure 3. The

load cells shall be located between the test body and

the grasping arms. The weight of each grasping arm

shall be 1.0 kg ± 3%.

6.4.2 Added weights: For Test B, two customary

10.0 kg ± 0.1 kg dumb-bell weights shall be added

with the help of specific appliances to each side of the

pendulum, for an additional weight on the pendulum

of 20.0 kg ± 0.2 kg. See Figure 3 for the location of

the specific appliances.

6.4.3 Pendulum fixation - The pendulum fixation to

the bar shall meet the following criteria:

6.4.3.1 Functional properties: The fixation shall al-

low an immediate transfer of forces between pendu-

lum and bar and guarantee a low-friction rotation of

the pendulum about the longitudinal axis of the bar

(the use of roll bearings is recommended).

6.4.3.2 Friction of the bar-pendulum fixation - The

frictional properties of the fixation shall meet the fol-

lowing criteria: The time for the pendulum (80 kg:

40 kg pendulum with additional 20 kg falling weight

at the inside bottom [no internal drop height] and

20 kg added weights) to swing from horizontal posi-

tion (release) through hanging (vertical) position shall

be 680 ms ± 15 ms.

6.4.4 Additional falling weight - The additional fal-

ling weight shall meet the following criteria:

6.4.4.1 Mass and geometry: The cylindrical falling

weight shall have a mass of 20.0 kg ± 0.2 kg and a

geometry as specified in Figure 4.

FIG International Gymnastics Federation

Standard Specification for Horizontal Bars

MAG – Men Artistic Gymnastics

IV

MAG 6

29.03.1996

4

Figure 4: Geometry of Additional Falling Load

(All dimensions with an accuracy of 3%)

erted on the pendulum simultaneously with the dis-

placement - time trace is acceptable. The total system,

detection and recording, shall be capable of measur-

ing reaction forces of up to 5000 N at frequencies

from 2 to 200 Hz to an accuracy of ± 1%. The mini-

mum sampling rate of the data acquisition system

shall be 500 Hz.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of a complete horizontal bar as it is intended

to be used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG6.

8 Conditioning and Test Temperature

8.1 The horizontal bar, mounted and assembled for

use, shall be preconditioned at 50% ± 10% relative

humidity and 21° C ± 3° C for a minimum of 24 hours

prior to the test. All testing shall be carried out under

the same conditions.

9 Laboratory Procedure (Test Method)

9.1 General set-up:

9.1.1 Mount the horizontal bar to a height as pre-

scribed for competitions (Part II).

9.1.2 The default cable tension shall be 1500 N

± 50 N provided that there is no other specific cable

tension suggested by the manufacturer. If a specific

cable tension is suggested by the manufacturer, then

this suggested cable tension shall be used.

9.1.3 Install the displacement measuring device on

the unloaded bar and determine the starting position.

9.2 Test A - Static traction stress:

9.2.1 Pull the midpoint of the bar vertically down-

wards with a static tractive force of 2200 N ± 20 N

and capture, then record the resulting maximum de-

flection (mm) using recording equipment described in

Section 6.5.

9.2.2 After the release of the static tractive force

verify whether the bar returns into the starting posi-

tion.

9.3 Test B - Stress by pendulum swing:

9.3.1 Attach the pendulum (80 kg: 40 kg pendulum

with additional 20 kg falling weight and 20 kg added

weights) to the bar in hanging position.

9.3.2 Move the pendulum from hanging position

into horizontal position and move the additional fal-

ling weight inside the pendulum to the 90 cm ± 1 cm

internal drop height position.

9.3.3 Release the pendulum and capture the two-

dimensional displacement - time history of the mid-

point of the bar and the reaction force - time history

of the pendulum, using recording equipment de-

6.4.4.2 Friction within the tube of the test body -

The frictional properties of the additional falling

weight shall meet the following criteria: The time for

the additional falling weight to cover the internal drop

height of 90 cm by a pendulum swing (80 kg) down

from horizontal position (release) shall be 640 ms

± 10 ms.

6.4.4.3 Damping of the additional falling weight at

the inside bottom of the tubular test body - The damp-

ing properties of the additional falling weight shall

meet the following criteria: The additional falling

weight (20 kg) shall produce an average peak force of

5800 N ± 1500 N over 15 impact tests inside the tu-

bular test body with a vertical drop height of 50 mm

± 1 mm. A chloroprene rubber at the bottom of the

test body with a thickness of 8 mm, a density of

1.40 g/cm3 and a tensile strength of 5,5 MPa is re-

commended.

6.5 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.5.1 Displacement - time: The selection of the

specific displacement - time recording equipment, in-

cluding transducers and recorders, is at the discretion

of the test laboratory. However, the transducers shall

provide linear signals proportional to the two-

dimensional displacement of the midpoint of the bar.

If displacement is recorded, the test equipment shall

have means to determine and record the starting posi-

tion of the bar from which the total deflections are

determined. The total system, detection and re-

cording, shall be capable of measuring displacements

of up to 200 mm at frequencies from 2 to 200 Hz to

an accuracy of ± 1%. The minimum sampling rate of

the data acquisition system shall be 500 Hz.

6.5.2 Reaction force - time: Any reaction force -

time recording equipment, including load cells and

recorders, which can monitor the reaction force ex-

FIG International Gymnastics Federation

Standard Specification for Horizontal Bars

MAG – Men Artistic Gymnastics

scribed in Section 6.5.

9.3.4 Stress the horizontal bar by repeating the pen-

dulum swing five times.

9.3.5 Immediately following each test, record the

following measurements: Fmax (N), positive vertical

deflection (mm), as well as positive and negative

horizontal deflection (mm).

9.3.6 All five tests shall be used to determine the

arithmetic mean value of each measured variable.

9.4 Test C - Oscillation damping:

9.4.1 Attach the pendulum (60 kg: 40 kg pendulum

with additional 20 kg falling weight at the inside bot-

tom of the pendulum) to the bar in hanging position.

9.4.2 Pull down the pendulum vertically until the

initial tension of 1000 N ± 30 N is reached.

9.4.3 Release the pendulum and capture the dis-

placement - time history of the midpoint of the bar

using recording equipment described in Section 6.5.

9.4.4 Repeat the above process five times.

9.4.5 Immediately following each test, record the

following measurements: Frequency (Hz) and half

amplitude interval (ms) of the oscillation.

9.4.6 All five tests shall be used to determine the

arithmetic mean value of each measured variable.

9.5 Calculate the values of all required variables

rounded to the decimal places of the corresponding

figures identified in Section 5.

10 Report

10.1 The test report shall include the following in-

IV

MAG 6

29.03.1996

5

formation:

10.1.1 Complete identification of the tested hori-

zontal bar, including type, source, manufacturer’s

model number (if appropriate), dimensions of test

specimen, and any other pertinent information. Pho-

tographs may be included in the test report for sample

documentation purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Test height and cable tension of the

unloaded horizontal bar.

10.1.6 Test A - Static traction stress: Description of

the static tractive force.

10.1.7 Test B - Stress by pendulum swing: Descrip-

tion of the pendulum mass with added weights, the

additional falling weight and the internal drop height.

10.1.8 Test C - Oscillation damping: Description of

the pendulum mass (including the additional falling

weight at the inside bottom of the pendulum) and the

initial tension.

10.1.9 Description of the test results relative to the

performance requirements identified in Section 5.

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

6

FIG International Gymnastics Federation

Standard Specification for 20 cm Landing Mats

MAG – Men Artistic Gymnastics

IV

MAG 11

01.08.1996

1

Standard Specification: 20 cm Landing Mats for Men Artistic

Gymnastics

This standard is issued under the fixed designation FIG: IV-MAG11-01.08.1996; the numbers immediately fol-

lowing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last

revision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test

laboratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of landing mats

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain shock-absorbing characteristics, the impact

force - time relationships, and the rebound properties

of 20 cm landing mats. This standard specification is

applicable to all landing mat systems that are to be

used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a landing mat system

which complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG11.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Base plane: The starting reference plane of

the landing mat system from which the total deflec-

tion and total height of rebound is determined. It is

taken as the top plane of the landing mat system.

3.1.3 Deflection: The measured distance (in mm)

between the base plane and the maximum displace-

ment of the impactor below the base plane.

3.1.4 Force (F): The product of the mass of the im-

pactor, expressed in kg, and the acceleration of the

impactor, expressed in m/s2.

3.1.5 Maximum Force (Fmax): The maximum value

of force measured during the impact and expressed in

Newtons.

3.1.6 Height of rebound: The measured distance (in

mm) between the base plane and the maximum dis-

placement of the impactor above the base plane.

3.1.7 Impactor: The striking part of the test appara-

tus.

3.1.8 Impact velocity: The velocity of the impactor,

expressed in m/s, immediately prior to crossing the

base plane on impact.

3.1.9 Theoretical drop height: A calculated drop

height which equates the measured velocity of the im-

pactor at the moment of impact to a height that would

generate the same velocity if the test were performed

at sea level and there was no friction to retard the im-

pactor during a drop from that height.

4 Principle of Measurement

4.1 A test specimen is impacted at a specified ve-

locity with an impactor of given mass and geometry.

A transducer mounted in the impactor monitors the

acceleration – time history of the impactor which is

recorded with the aid of a data acquisition system. An

additional transducer may be used to monitor the dis-

placement – time history of the impactor.

4.2 Dynamic data obtained during these procedures

are indicative of the cushioning and rebound proper-

ties of the landing mat systems and materials used in

training and FIG-sanctioned competitions.

5 Performance Requirements

5.1 When tested according to the procedures de-

scribed in Section 9, the overall mean values of the

measured variables across all impact sites shall be

within the figures of Table 1.

Table 1: Figures for 20 cm Landing Mats

Deflection

(mm)

≤110

Height of rebound

(mm)

≤90

Fmax

(N)

≤3000

FIG International Gymnastics Federation

Standard Specification for 20 cm Landing Mats

MAG – Men Artistic Gymnastics

6 Test Apparatus

6.1 Impact test machine: Any type of dynamic test-

ing apparatus that is capable of impacting a test

specimen at a prescribed impact velocity and moni-

tors and records the acceleration - time history of the

impactor is acceptable. The impact test machine and

the impactor shall have sufficient rigidity to eliminate

undesirable vibrations in the apparatus which might

be recorded on the acceleration - time curve. The im-

pact test machine shall also be designed in such a

manner that only the impact face of the impactor con-

tacts the test specimen at any time during the test pro-

cedures.

6.2 Impactor: The impactor shall be 20 kg ±0.2 kg

and shall have a flat impact face with a 10 cm ±

0.5 cm diameter. The edge of the impactor face

should be relieved to eliminate sharp edges. Provision

shall be made so that the accelerometer can be se-

curely fastened parallel to the vertical axis of the im-

pactor with a maximum deviation of ±5o.

6.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.3.1 Acceleration - time: The selection of the spe-

cific acceleration - time recording equipment, includ-

ing transducers and recorders, is at the discretion of

the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the peak acceleration value to an accuracy of ±5% of

the true value. The total system, detection and re-

cording, shall be capable of measuring impact accel-

erations of up to 200 g at frequencies from 2 to

1000 Hz to an accuracy of ±5%. The minimum sam-

pling rate of the data acquisition system shall be 5000

Hz.

6.3.2 Displacement - time: It is optional, but desir-

able, that the displacement - time history is recorded

by a separate transducer. Any transducer that provides

a linear signal proportional to the displacement of the

impactor along the impact axis which can be moni-

tored simultaneously with the acceleration - time trace

is acceptable. If displacement is recorded, the test

equipment shall have means to determine and record

the top plane (base plane) of the test specimen from

which the total deformation and rebound height are

determined.

6.3.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

7 Test Specimen

7.1 The test specimen submitted for testing shall

IV

MAG 11

01.08.1996

2

represent the landing mat as it is intended to be used

during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG11. Exception: See 7.3..

7.3 The minimum horizontal dimensions (length *

width) for any test specimen shall be 200 cm * 120

cm.

8 Conditioning and Test Temperature

8.1 Test specimens shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 Impact locations: A total of nine impact sites

shall be designated on the test specimen. See Figure 1

for an illustration of the impact sites.

Figure 1: Impact Locations for Landing Mats

9.2 Impact test procedures:

9.2.1 Place the test specimen under the impact test

machine on a smooth, solid floor (concrete or metal

plate) and orient the impactor such that the centre of

the impact face will contact one of the designated im-

pact test sites.

9.2.2 Raise the impactor to an appropriate drop

height such that it will contact the test specimen with

an impact velocity of 3.96 m/s ±3%. This corre-

sponds to a theoretical drop height of 0.8 m.

9.2.3 Release the impactor and capture the accel-

eration - time history and displacement - time history

(if applicable) using recording equipment described in

Section 6.3.

9.2.4 Upon completion of a given impact test, raise

the impactor off the surface of the test specimen.

9.2.5 The duration between tests at a given impact

site shall not be less than 120 seconds.

9.2.6 Each test specimen shall receive a total of 90

impacts. Impact each of the nine impact sites ten

times.

FIG International Gymnastics Federation

Standard Specification for 20 cm Landing Mats

MAG – Men Artistic Gymnastics

9.3 Calculations:

9.3.1 Immediately following each test, record the

following measurements: Fmax (N), Deflection (mm)

and Height of rebound (mm).

9.3.2 The last eight tests for each impact site shall

be used to determine the arithmetic mean value of a

measured variable for each impact site and for the

overall mean value of a measured variable across all

impact sites.

9.3.3 Calculate the mean values of Deflection,

Height of rebound and Fmax across all impact sites

rounded to zero decimal places.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested landing

mat, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

IV

MAG 11

01.08.1996

3

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Description of the impactor mass and the

drop height conditions.

10.1.6 Description of the test results relative to the

performance requirements identified in Section 5.

10.1.7 Mean values of Deflection, Height of re-

bound and Fmax across all impact sites.

10.1.8 Maximum value, minimum value and stan-

dard deviation of Deflection, Height of rebound and

Fmax variables.

10.1.9 Mean values of Deflection, Height of re-

bound and Fmax for the last eight tests at each impact

site.

10.1.10 Deflection, Height of rebound and Fmax val-

ues for all tests.

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

4

FIG International Gymnastics Federation

Standard Specification for 10 cm Landing Mat

MAG – Men Artistic Gymnastics

IV

MAG 12

12.07.1989

1

Standard Specification: 10 cm Landing Mats for Men Artistic

Gymnastics

This standard is issued under the fixed designation FIG: IV-MAG12-12.07.1989; the numbers immediately fol-

lowing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last

revision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test

laboratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of landing mats

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain shock-absorbing characteristics, the impact

force - time relationships, and the rebound properties

of 10 cm landing mats. This standard specification is

applicable to all landing mat systems that are to be

used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a landing mat system

which complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG12.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Base plane: The starting reference plane of

the landing mat system from which the total deflec-

tion and total height of rebound is determined. It is

taken as the top plane of the landing mat system.

3.1.3 Deflection: The measured distance (in mm)

between the Base plane and the maximum displace-

ment of the impactor below the Base plane.

3.1.4 Force (F): The product of the mass of the im-

pactor, expressed in kg, and the acceleration of the

impactor, expressed in m/s2.

3.1.5 Maximum Force (Fmax): The maximum value

of force measured during the impact and expressed in

Newtons.

3.1.6 Height of rebound: The measured distance (in

mm) between the Base plane and the maximum dis-

placement of the impactor above the Base plane.

3.1.7 Impactor: The striking part of the test appara-

tus.

3.1.8 Impact velocity: The velocity of the impactor,

expressed in m/s, immediately prior to crossing the

base plane on impact.

3.1.9 Theoretical drop height: A calculated drop

height which equates the measured velocity of the im-

pactor at the moment of impact to a height that would

generate the same velocity if the test were performed

at sea level and there was no friction to retard the im-

pactor during a drop from that height.

4 Principle of Measurement

4.1 A test specimen is impacted at a specified ve-

locity with an impactor of given mass and geometry.

A transducer mounted in the impactor monitors the

acceleration – time history of the impactor which is

recorded with the aid of a data acquisition system. An

additional transducer may be used to monitor the dis-

placement – time history of the impactor.

4.2 Dynamic data obtained during these procedures

are indicative of the cushioning and rebound proper-

ties of the landing mat systems and materials used in

training and FIG-sanctioned competitions.

5 Performance Requirements

5.1 When tested according to the procedures de-

scribed in Section 9, the overall mean values of the

measured variables across all impact sites shall be

within the figures of Table 1.

Table 1: Figures for 10 cm Landing Mats

Deflection

(mm)

≤65

Height of rebound

(mm)

≤80

Fmax

(N)

≤3750

FIG International Gymnastics Federation

Standard Specification for 10 cm Landing Mat

MAG – Men Artistic Gymnastics

6 Test Apparatus

6.1 Impact test machine: Any type of dynamic test-

ing apparatus that is capable of impacting a test

specimen at a prescribed impact velocity and monitor-

ing and recording the acceleration - time history of

the impactor is acceptable. The impact test machine

and the impactor shall have sufficient rigidity to

eliminate undesirable vibrations in the apparatus

which might be recorded on the acceleration - time

curve. The impact test machine shall also be designed

in such a manner that only the impact face of the im-

pactor contacts the test specimen at any time during

the test procedures.

6.2 Impactor: The impactor shall be 20 kg ±0.2 kg

and shall have a flat impact face with a 10 cm ±

0.5 cm diameter. The edge of the impactor face

should be relieved to eliminate sharp edges. Provision

shall be made so that the accelerometer can be se-

curely fastened parallel to the vertical axis of the im-

pactor with a maximum deviation of ±5o.

6.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.3.1 Acceleration - time: The selection of the spe-

cific acceleration - time recording equipment, includ-

ing transducers and recorders, is at the discretion of

the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the peak acceleration value to an accuracy of ±5% of

the true value. The total system, detection and re-

cording, shall be capable of measuring impact accel-

erations of up to 200 g at frequencies from 2 to

1000 Hz to an accuracy of ±5%. The minimum sam-

pling rate of the data acquisition system shall be 5000

Hz.

6.3.2 Displacement - time: It is optional, but desir-

able, that the displacement - time history is recorded

by a separate transducer. Any transducer that provides

a linear signal proportional to the displacement of the

impactor along the impact axis which can be moni-

tored simultaneously with the acceleration - time trace

is acceptable. If displacement is recorded, the test

equipment shall have means to determine and record

the top plane (base plane) of the test specimen from

which the total deformation and rebound height are

determined.

6.3.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

7 Test Specimen

7.1 The test specimen submitted for testing shall

IV

MAG 12

12.07.1989

2

represent the landing mat as it is intended to be used

during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG12. Exception: See 7.3.

7.3 The minimum horizontal dimensions (length *

width) for any test specimen shall be 200 cm * 120

cm.

8 Conditioning and Test Temperature

8.1 Test specimens shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 Impact locations: A total of nine impact sites

shall be designated on the test specimen. See Figure 1

for an illustration of the impact sites.

Figure 1: Impact Locations for Landing Mats

9.2 Impact test procedures:

9.2.1 Place the test specimen under the impact test

machine on a smooth, solid floor (concrete or metal

plate) and orient the impactor such that the centre of

the impact face will contact one of the designated im-

pact test sites.

9.2.2 Raise the impactor to an appropriate drop

height such that it will contact the test specimen with

an impact velocity of 2.80 m/s +/- 3%. This corre-

sponds to a theoretical drop height of 0.4 m.

9.2.3 Release the impactor and capture the accel-

eration - time history and displacement - time history

(if applicable) using recording equipment described in

Section 6.3.

9.2.4 Upon completion of a given impact test, raise

the impactor off the surface of the test specimen.

9.2.5 The duration between tests at a given impact

site shall not be less than 120 seconds.

9.2.6 Each test specimen shall receive a total of 90

impacts. Impact each of the nine impact sites ten

times.

FIG International Gymnastics Federation

Standard Specification for 10 cm Landing Mat

MAG – Men Artistic Gymnastics

9.3 Calculations:

9.3.1 Immediately following each test, record the

following measurements: Fmax (N), Deflection (mm)

and Height of rebound (mm).

9.3.2 The last eight tests for each impact site shall

be used to determine the arithmetic mean value of a

measured variable for each impact site and for the

overall mean value of a measured variable across all

impact sites.

9.3.3 Calculate the mean values of Deflection,

Height of rebound and Fmax across all impact sites

rounded to zero decimal places.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested landing

mat, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

IV

MAG 12

12.07.1989

3

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Description of the impactor mass and the

drop height conditions.

10.1.6 Description of the test results relative to the

performance requirements identified in Section 5.

10.1.7 Mean values of Deflection, Height of re-

bound and Fmax across all impact sites.

10.1.8 Maximum value, minimum value and stan-

dard deviation of Deflection, Height of rebound and

Fmax variables.

10.1.9 Mean values of Deflection, Height of re-

bound and Fmax for the last eight tests at each impact

site.

10.1.10 Deflection, Height of rebound and Fmax val-

ues for all tests.

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

4

FIG International Gymnastics Federation

Standard Specification for Vaulting Boards

MAG – Men Artistic Gymnastics

IV

MAG 14

01.01.2006

1

Standard Specification: Vaulting Boards for Men Artistic Gymnastics

This standard is issued under the fixed designation FIG: IV-MAG14-01.07.1985; the numbers immediately fol-

lowing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last

revision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test

laboratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of vaulting

boards and to minimize any differences between

competition and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain shock-absorbing characteristics, the impact

force - time relationships, and the rebound properties

of vaulting boards. This standard specification is ap-

plicable to all vaulting boards that are to be used at

any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a vaulting board which

complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-MAG14.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Starting position of an impact site: The verti-

cal position of an impact site at the surface of an

unloaded vaulting board from which the total deflec-

tion and total height of rebound is determined.

3.1.3 Deflection: The measured distance (in mm)

between the starting position of an impact site and the

maximum displacement of the impactor below the

starting position of an impact site.

3.1.4 Force (F): The product of the mass of the im-

pactor, expressed in kg, and the acceleration of the

impactor, expressed in m/s2.

3.1.5 Maximum Force (Fmax): The maximum value

of force measured during the impact and expressed in

Newtons.

3.1.6 Height of rebound: The measured distance (in

mm) between the starting position of an impact site

and the maximum displacement of the impactor above

the starting position of an impact site.

3.1.7 Impactor: The striking part of the test appara-

tus.

3.1.8 Impact velocity: The velocity of the impactor,

expressed in m/s, immediately prior to crossing the

starting position of an impact site on impact.

3.1.9 Theoretical drop height: A calculated drop

height which equates the measured velocity of the im-

pactor at the moment of impact to a height that would

generate the same velocity if the test were performed

at sea level and there was no friction to retard the im-

pactor during a drop from that height.

4 Principle of Measurement

4.1 A test specimen is impacted at a specified ve-

locity with an impactor of given mass and geometry.

A transducer mounted in the impactor monitors the

acceleration – time history of the impactor which is

recorded with the aid of a data acquisition system. An

additional transducer may be used to monitor the dis-

placement – time history of the impactor.

4.2 Dynamic data obtained during these procedures

are indicative of the cushioning and rebound proper-

ties of the vaulting board used in training and FIG-

sanctioned competitions.

5 Performance Requirements

5.1 When tested according to the procedures de-

scribed in Section 9, the overall mean values of the

measured variables and the differences of the mean

values at specified impact sites shall be within the

figures of Table 1.

FIG International Gymnastics Federation

Standard Specification for Vaulting Boards

MAG – Men Artistic Gymnastics

Table 1: Figures for the “hard” Vaulting Boards

See Figure 1 for an illustration of the impact sites.

X represents the overall mean value of the measured vari-

able.

Deflection

(mm)

Mean value across

impact sites 1 to 5

Difference be-

tween highest and

lowest mean value

on impact sites 1

to 5

Difference be-

tween mean value

on impact sites 6

and 7

Height of re-

bound

(mm)

340 ≤x ≤400

Fmax

(N))

IV

MAG 14

01.01.2006

2

55 ≤x ≤68

x ≤4000

≤15

≤100

≤4

≤25

≤150

Table 2: Figures for the “soft” Vaulting Boards

See Figure 1 for an illustration of the impact sites.

X represents the overall mean value of the measured vari-

able.

Deflection

(mm)

Mean value across

impact sites 1 to 5

Difference be-

tween highest and

lowest mean value

on impact sites 1

to 5

Difference be-

tween mean value

on impact sites 6

and 7

Height of re-

bound

(mm)

340 ≤x ≤400

Fmax

(N))

62 ≤x ≤80

x ≤4000

≤15

≤100

≤4

≤25

≤150

curely fastened parallel to the vertical axis of the im-

pactor with a maximum deviation of ±5o.

6.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.3.1 Acceleration - time: The selection of the spe-

cific acceleration - time recording equipment, includ-

ing transducers and recorders, is at the discretion of

the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the peak acceleration value to an accuracy of ±5% of

the true value. The total system, detection and re-

cording, shall be capable of measuring impact accel-

erations of up to 200 g at frequencies from 2 to

1000 Hz to an accuracy of ±5%. The minimum sam-

pling rate of the data acquisition system shall be 5000

Hz.

6.3.2 Displacement - time: It is optional, but desir-

able, that the displacement - time history is recorded

by a separate transducer. Any transducer that provides

a linear signal proportional to the displacement of the

impactor along the impact axis which can be moni-

tored simultaneously with the acceleration - time trace

is acceptable. If displacement is recorded, the test

equipment shall have means to determine and record

the starting position of an impact site of the test

specimen from which the total deformation and re-

bound height are determined.

6.3.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of a vaulting board as it is intended to be used

during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-MAG14.

8 Conditioning and Test Temperature

8.1 The test specimen shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 Impact locations: A total of seven impact sites

shall be designated on the test specimen. See Figure 1

for an illustration of the impact sites.

6 Test Apparatus

6.1 Impact test machine: Any type of dynamic test-

ing apparatus that is capable of impacting a test

specimen at a prescribed impact velocity and monitor-

ing and recording the acceleration - time history of

the impactor is acceptable. The impact test machine

and the impactor shall have sufficient rigidity to

eliminate undesirable vibrations in the apparatus

which might be recorded on the acceleration - time

curve. The impact test machine shall also be designed

in such a manner that only the impact face contacts

the test specimen at any time during the test proce-

dures.

6.2 Impactor: The impactor shall be 20 kg ±0.2 kg

and shall have a flat impact face with a 10 cm ±

0.5 cm diameter. The edge of the impactor face

should be relieved to eliminate sharp edges. Provision

shall be made so that the accelerometer can be se-

FIG International Gymnastics Federation

Standard Specification for Vaulting Boards

MAG – Men Artistic Gymnastics

Figure 1: Impact Locations for Vaulting Boards

IV

MAG 14

01.01.2006

3

(Dimensions in cm)

and Height of rebound (mm).

9.3.2 The last eight tests for each impact site shall

be used to determine the arithmetic mean value of a

measured variable for each measurement point.

9.3.3 Calculate the mean values of Deflection,

Height of rebound and Fmax across all impact sites

rounded to zero decimal places.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested vaulting

board, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Description of the impactor mass and the

drop height conditions.

10.1.6 Description of the test results relative to the

performance requirements identified in Section 5.

10.1.7 Mean values of Deflection, Height of re-

bound and Fmax across impact sites 1 to 5.

10.1.8 Maximum value, minimum value and stan-

dard deviation of Deflection, Height of rebound and

Fmax variables for impact sites 1 to 5.

10.1.9 Mean values of Deflection, Height of re-

bound and Fmax for the last eight tests at each impact

site.

10.1.10 Deflection, Height of rebound and Fmax val-

ues for all tests.

9.2 Impact test procedures:

9.2.1 Place the test specimen under the impact test

machine on a smooth, solid floor (concrete or metal

plate) and orient the impactor such that the centre of

the impact face will contact one of the designated im-

pact test sites.

9.2.2 Raise the impactor to an appropriate drop

height such that it will contact the test specimen with

an impact velocity of 3.96 m/s ±3%. This corre-

sponds to a theoretical drop height of 0.8 m.

9.2.3 Release the impactor and capture the accel-

eration - time history and displacement - time history

(if applicable) using recording equipment described in

Section 6.3.

9.2.4 Upon completion of a given impact test, raise

the impactor off the surface of the test specimen.

9.2.5 The duration between tests at a given impact

site shall not be less than 30 seconds.

9.2.6 Each test specimen shall receive a total of 70

impacts. Impact each of the seven impact sites ten

times.

9.3 Calculations:

9.3.1 Immediately following each test, record the

following measurements: Fmax (N), Deflection (mm)

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

4

FIG International Gymnastics Federation

Standard Specification for Vaulting Tables

WAG – Women Artistic Gymnastics

IV

WAG 1

01.02.2001

1

Standard Specification: Vaulting Table for Women Artistic Gymnastics

This standard is issued under the fixed designation FIG: IV-WAG1-18.04.1989; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

The standard specifications for vaulting tables for women artistic gymnastics are the same as

for men artistic gymnastics, therefore, this standard refers to the FIG standard IV-MAG4.

See:

IV

MAG 4

01.02.2001

1-3

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

2

FIG International Gymnastics Federation

Standard Specification for Uneven Bars

WAG – Women Artistic Gymnastics

IV

WAG 2

01.05.1993

1

Standard Specification: Uneven Bars for Women Artistic Gymnastics

This standard is issued under the fixed designation FIG: IV-WAG2-01.05.1993; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of uneven bars

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain static stiffness properties, dynamic force - time

and displacement - time relationships and the oscilla-

tion characteristics of uneven bars. This standard

specification is applicable to all uneven bars that are

to be used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using uneven bars which

comply with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-WAG2.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: IV-MAG6.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Cable tension: The predetermined value of

force (in N) exerted on the mounting cables of the

completely-mounted unloaded uneven bars.

3.1.2 Static tractive force: The predetermined value

of force (in N) exerted on the midpoint of a bar, pull-

ing the bar vertically downwards.

3.1.3 Starting position: The position of an unloaded

bar from which the total deflection in vertical and

horizontal direction is determined. The midpoint of

the bar shall serve as the point of reference for the

measurements.

3.1.4 Deflection: The measured distance (in mm)

between the starting position and the maximum dis-

placement of the midpoint of a bar in vertical and

horizontal direction respectively.

3.1.5 Definition of spatial dimensions: For the de-

termination of the vertical and horizontal deflection of

the midpoint of a bar the spatial dimensions are de-

fined as illustrated in Figure 1.

Figure 1: Definition of Spatial Dimensions

(Pendulum in horizontal position before release)

3.1.6 Pendulum: Tubular test body of given dimen-

sions and mass with an additional low-friction falling

weight inside. The test body is attached to a bar with

the help of two inflexible grasping arms, each of

which is at the same distance from the midpoint of the

bar, guaranteeing a low-friction rotation of the test

body about the longitudinal axis of the bar.

3.1.7 Maximum Force (Fmax): The maximum value

of the reaction force in the direction of the pendulum's

centre of gravity measured as the sum of the forces

exerted on both grasping arms during the pendulum

swing, expressed in Newtons.

3.1.8 Hanging position: Stable equilibrium position

of the hanging pendulum under gravity conditions

only.

3.1.9 Horizontal position: Position of the attached

pendulum rectangular to the hanging position.

3.1.10 Additional falling weight: Cylindrical test

body of given dimensions and mass inside the pendu-

lum producing an additional impact stress on the

gymnastic apparatus during pendulum swing.

3.1.11 Internal drop height: Predetermined sliding

distance of the additional falling weight inside the

pendulum.

3.1.12 Initial tension: Predetermined value of the

force exerted on a bar, composed of the gravity of the

FIG International Gymnastics Federation

Standard Specification for Uneven Bars

WAG – Women Artistic Gymnastics

attached pendulum and an additional tractive force

pulling the bar-pendulum system vertically down-

wards.

3.1.13 Frequency of oscillation: Reciprocal of the

value determined by the duration of the half ampli-

tude interval divided by the number of oscillations of

a bar-pendulum system within the half amplitude in-

terval. The frequency is expressed in Hertz. See Fig-

ure 2 for illustration of the frequency determination.

3.1.14 Maximum amplitude: Value of the amplitude

(in mm) of the first oscillation of a bar-pendulum sys-

tem after the release of the initial tension.

3.1.15 Half amplitude: Value of the amplitude

(in mm) of the first oscillation which is equal to or

less than half the maximum amplitude.

3.1.16 Half amplitude interval: Duration of oscilla-

tion (in ms) between the passage of the maximum

amplitude and the reaching of the half amplitude. See

Figure 2 for illustration.

Figure 2: Oscillation Damping Parameters

IV

WAG 2

01.05.1993

2

tional falling weight inside the tubular pendulum

slides down from a predetermined internal drop

height until the weight strikes against the inside bot-

tom of the pendulum, producing an additional impact

stress on the gymnastic apparatus. A measuring de-

vice monitors the two-dimensional displacement -

time history of the midpoint of the bar. Load cells in-

side both pendulum grasping arms monitor the reac-

tion force - time history of the pendulum. Both are

recorded with the aid of a data acquisition system.

The test measures the maximum reaction force in the

direction of the pendulum's centre of gravity as well

as the positive deflection of the bar in vertical direc-

tion and the positive and negative deflection of the

bar in horizontal direction.

4.1.3 Test C - Oscillation damping: A pendulum

which is attached to a bar of a mounted apparatus is

pulled vertically downwards until a predetermined

initial tension is reached. The abrupt release causes a

damped oscillation of the bar-pendulum system. A

measuring device monitors the displacement - time

history of the midpoint of the bar which is recorded

with the aid of a data acquisition system. The test

measures the frequency as well as the half amplitude

interval of the oscillation.

4.2 Static and dynamic data obtained during these

procedures are indicative of the static stiffness, elas-

tic, damping, and oscillation properties of the uneven

bars used in training and FIG-sanctioned competi-

tions.

5 Performance Requirements

5.1 Test A - Static traction stress: When tested ac-

cording to the procedures described in Section 9.2,

the values of the measured variables shall be within

the figures of Table 1.

Table 1: Figures for Test A – Static traction stress

x represents the measured variable

Test A: Static traction stress

Upper bar

Deflection (mm)

Lower bar

Deflection (mm)

70 ≤x ≤100

70 ≤x ≤100

4 Principle of Measurement

4.1 The complete measurement is composed of

three specific test procedures:

4.1.1 Test A - Static traction stress: A bar of a

mounted apparatus is pulled vertically downwards

with a predetermined static tractive force. A measur-

ing device mounted on the bar monitors the displace-

ment - time history of the midpoint of the bar caused

by this force. The maximum deflection is recorded

with the aid of a data acquisition system. After the

release of the static tractive force the bar must return

into the starting position.

4.1.2 Test B - Stress by pendulum swing: A pendu-

lum which is attached to a bar of a mounted apparatus

is rotated from hanging position into horizontal posi-

tion and then released. While it swings down, an addi-

5.2 Test B - Stress by pendulum swing: When tested

according to the procedures described in Section 9.3,

the mean values of the measured variables shall be

within the figures of Table 2.

FIG International Gymnastics Federation

Standard Specification for Uneven Bars

WAG – Women Artistic Gymnastics

Table 2: Figures for Test B – Stress by pendulum swing

x represents the mean value of the measured variable

Test B: Stress by pendulum swing

Upper bar

Fmax (N)

Positive vertical deflection (mm)

Negative horizontal deflection (mm)

Positive horizontal deflection (mm)

Lower bar

Fmax (N)

Positive vertical deflection (mm)

Negative horizontal deflection (mm)

Positive horizontal deflection (mm)

1500 ≤x ≤1800

90 ≤x ≤130

-25 ≤x ≤-40

50 ≤x ≤75

1500 ≤x ≤1800

90 ≤x ≤130

-25 ≤x ≤-40

50 ≤x ≤75

IV

WAG 2

01.05.1993

3

tem is released from a magnet at the prescribed initial

tension.

6.4 Pendulum - The pendulum shall meet the fol-

lowing criteria:

6.4.1 Mass and geometry: The tubular test body

shall have a mass of 40.0 kg ± 3% (including load

cells, grasping arms and appliances for additional

weights) and a geometry as specified in Figure 3. The

load cells shall be located between the test body and

the grasping arms. The weight of each grasping arm

shall be 1.0 kg ± 3%.

Figure 3: Geometry of Tubular Test Body

(All dimensions with an accuracy of 3%)

5.3 Test C - Oscillation damping: When tested ac-

cording to the procedures described in Section 9.4,

the mean values of the measured variables shall be

within the figures of Table 3.

Table 3: Figures for Test C – Oscillation damping

x represents the mean value of the measured variable

Test C: Oscillation damping

Upper bar

Frequency of oscillation (Hz)

Half amplitude interval (ms)

Lower bar

Frequency of oscillation (Hz)

Half amplitude interval (ms)

2.50 ≤x ≤3.50

350 ≤x ≤5700

2.50 ≤x ≤3.50

350 ≤x ≤5700

6 Test Set-up and Apparatus

6.1 Set-up for Test A - Static traction stress: Any

type of test set-up is acceptable that is capable to

stress the test specimen under prescribed conditions

and monitoring and recording the displacement - time

history of the midpoint of the bar.

6.2 Set-up for Test B - Stress by pendulum swing:

Any type of test set-up is acceptable that is capable of

stressing the test specimen with a pendulum swing

under prescribed conditions and monitoring and re-

cording the displacement - time history of the mid-

point of the bar and the reaction force - time history

of the pendulum. It is optional, but desirable, that the

pendulum is released from a magnet in the horizontal

position.

6.3 Set-up for Test C - Oscillation damping: Any

type of test set-up is acceptable that is capable of

stressing a bar-pendulum system under prescribed

conditions and monitoring and recording the dis-

placement - time history of the midpoint of the bar. It

is optional, but desirable, that the bar-pendulum sys-

6.4.2 Pendulum fixation - The pendulum fixation to

a bar shall meet the following criteria:

6.4.2.1 Functional properties: The fixation shall al-

low an immediate transfer of forces between pendu-

lum and bar and guarantee a low-friction rotation of

the pendulum about the longitudinal axis of the bar

(the use of roll bearings is recommended).

6.4.2.2 Friction of the bar-pendulum fixation - The

frictional properties of the fixation shall meet the cri-

teria as specified in FIG Apparatus Rules: IV-MAG6

Standard Specification for Horizontal Bars for Men

Artistic Gymnastics.

6.4.3 Additional falling weight - The additional fal-

ling weight shall meet the following criteria:

FIG International Gymnastics Federation

Standard Specification for Uneven Bars

WAG – Women Artistic Gymnastics

6.4.3.1 Mass and geometry: The cylindrical falling

weight shall have a mass of 10.0 kg ± 0.1 kg and a

geometry as specified in Figure 4.

Figure 4: Geometry of Additional Falling Load

(All dimensions with an accuracy of 3%)

IV

WAG 2

01.05.1993

4

from 2 to 200 Hz to an accuracy of ± 1%. The mini-

mum sampling rate of the data acquisition system

shall be 500 Hz.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of complete uneven bars as they are intended

to be used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-WAG2.

8 Conditioning and Test Temperature

8.1 The uneven parallel bars, mounted and assem-

bled for use, shall be preconditioned at 50% ± 10%

relative humidity and 21° C ± 3° C for a minimum of

24 hours prior to the test. All testing shall be carried

out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 General set-up:

9.1.1 Mount the upper and lower bar to heights as

prescribed for competitions (Part II). The inside width

between the bars shall be 1.79 m.

9.1.2 The default cable tension shall be 2750 N

± 50 N provided that there is no other specific cable

tension suggested by the manufacturer. If a specific

cable tension is suggested by the manufacturer, then

this suggested cable tension shall be used.

9.1.3 Install the displacement measuring device on

the unloaded bars and determine the starting posi-

tions.

9.2 Test A - Static traction stress:

9.2.1 Pull the midpoints of the upper and lower bar

individually vertically downwards with a static trac-

tive force of 1350 N ± 20 N and capture, then record

the resulting maximum deflections (mm) using re-

cording equipment described in Section 6.5.

9.2.2 After the release of the static tractive force

verify whether the bars return into the starting posi-

tion.

9.3 Test B - Stress by pendulum swing:

9.3.1 Attach the pendulum (50 kg: 40 kg pendulum

with additional 10 kg falling weight) to a bar in hang-

ing position.

9.3.2 Move the pendulum from hanging position

into horizontal position and move the additional fal-

ling weight inside the pendulum to the 50 cm ± 1 cm

internal drop height position. For the direction of the

pendulum swing at the upper and lower bar see Fig-

ure 1.

9.3.3 Release the pendulum and capture the two-

dimensional displacement - time history of the mid-

point of the bar and the reaction force - time history

of the pendulum, using recording equipment de-

6.4.3.2 Friction within the tube of the test body -

The frictional properties of the additional falling

weight shall meet the criteria as specified in FIG Ap-

paratus Rules: IV-MAG6 Standard Specification for

Horizontal Bars for Men Artistic Gymnastics.

6.4.3.3 Damping of the additional falling weight at

the inside bottom of the tubular test body - The damp-

ing properties of the additional falling weight shall

meet the criteria as specified in FIG Apparatus Rules:

IV-MAG6 Standard Specification for Horizontal Bars

for Men Artistic Gymnastics.

6.5 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.5.1 Displacement - time: The selection of the

specific displacement - time recording equipment, in-

cluding transducers and recorders, is at the discretion

of the test laboratory. However, the transducers shall

provide linear signals proportional to the two-

dimensional displacement of the midpoint of a bar. If

displacement is recorded, the test equipment shall

have means to determine and record the starting posi-

tion of the bar from which the total deflections are

determined. The total system, detection and re-

cording, shall be capable of measuring displacements

of up to 200 mm at frequencies from 2 to 200 Hz to

an accuracy of ± 1%. The minimum sampling rate of

the data acquisition system shall be 500 Hz.

6.5.2 Reaction force - time: Any reaction force -

time recording equipment, including load cells and

recorders, which can monitor the reaction force ex-

erted on the pendulum simultaneously with the dis-

placement - time trace is acceptable. The total system,

detection and recording, shall be capable of measur-

ing reaction forces of up to 5000 N at frequencies

FIG International Gymnastics Federation

Standard Specification for Uneven Bars

WAG – Women Artistic Gymnastics

scribed in Section 6.5.

9.3.4 Stress each bar by repeating the pendulum

swing five times.

9.3.5 Immediately following each test, record the

following measurements: Fmax (N), positive vertical

deflection (mm), as well as positive and negative

horizontal deflection (mm).

9.3.6 All five tests per bar shall be used to deter-

mine the arithmetic mean values of the measured

variables for each bar

9.4 Test C - Oscillation damping:

9.4.1 Attach the pendulum (50 kg: 40 kg pendulum

with additional 10 kg falling weight at the inside bot-

tom of the pendulum) to a bar in hanging position.

9.4.2 Pull down the pendulum vertically until the

initial tension of 1000 N ± 30 N is reached.

9.4.3 Release the pendulum and capture the dis-

placement - time history of the midpoint of the bar

using recording equipment described in Section 6.5.

9.4.4 Repeat the above process for each bar five

times.

9.4.5 Immediately following each test, record the

following measurements: Frequency (Hz) and half

amplitude interval (ms) of the oscillation.

9.4.6 All five tests per bar shall be used to deter-

mine the arithmetic mean values of the measured

variables for each bar.

9.5 Calculate the values of all required variables

rounded to the decimal places of the corresponding

figures identified in Section 5.

IV

WAG 2

01.05.1993

5

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested uneven

bars, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Test height and cable tension of the

unloaded horizontal bar.

10.1.6 Test A - Static traction stress: Description of

the Static tractive force.

10.1.7 Test B - Stress by pendulum swing: Descrip-

tion of the pendulum mass, the additional falling

weight and the internal drop height.

10.1.8 Test C - Oscillation damping: Description of

the pendulum mass (including the additional falling

weight at the inside bottom of the pendulum) and the

initial tension.

10.1.9 Description of the test results relative to the

performance requirements identified in Section 5.

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

6

FIG International Gymnastics Federation

Standard Specification for Balance Beams

WAG – Women Artistic Gymnastics

IV

WAG 3

01.12.1994

1

Standard Specification: Balance Beams for Women Artistic Gymnastics

This standard is issued under the fixed designation FIG: IV-WAG3-01.12.1994; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of balance beams

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of-

certain elastic and shock absorbing characteristics, as

well as frictional characteristics of balance beams.

This standard specification is applicable to all balance

beams that are to be used at any FIG-sanctioned

event.

1.2 This specification does not imply that an injury

cannot be incurred while using a balance beam which

complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-WAG3.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Base plane: The starting reference plane of

the balance beam from which deflection is deter-

mined. It is taken as the upper surface of the balance

beam loaded by the loading disk prior to any impact.

3.1.2 Deflection (D): The measured distance (in

mm) between the base plane and the bottom surface

of the loading disk during the impact.

3.1.3 Maximum deflection (Dmax): The maximum

value of deflection (in mm) measured during the im-

pact.

3.1.4 Force (F): The force applied to the balance

beam during the impact, expressed in Newtons.

3.1.5 Energy of deflection (E): The integration

value or calculated area under the force-deflection

curve expressed in Nm (Newton*meter). The domain

of integration is from the rising point to the maximum

point of deflection on the curve.

3.1.6 Rebound deflection (Dr): The maximum re-

bounding displacement (in mm) of the bottom surface

of the loading disk, measured from the plane of

maximum deflection.

3.1.7 Rebound time: The difference in time (in s)

between the point of maximum deflection and the

point of rebound deflection.

3.1.8 Rebound velocity (Vr): The quotient of re-

bound deflection and rebound time expressed in

mm/s.

3.1.9 Intensity of rebound (DrVr): The product of

rebound deflection and rebound velocity expressed in

mm2/s.

3.1.10 Loading disk: The part of the test apparatus

which applies the specified load to the test specimen.

3.1.11 Slider: A test body of given mass and ge-

ometry for measuring frictional characteristics of the

balance beam. The slider includes a test sole which is

bonded to the bottom of the slider and is made of syn-

thetic material with defined friction properties.

3.1.12 Maximum traction force: The maximum

statical friction force expressed in Newtons, observed

at the beginning of the pulling movement of the slider.

3.1.13 Friction coefficient of balance beam: Quo-

tient of the maximum traction force (in N) and the

weight of the slider (in N).

4 Principle of Measurement

4.1 The complete measurement procedure consists

of two specific test procedures:

4.1.1 Test A - Elasticity and shock absorption: A

specimen balance beam is impacted by dropping an

impactor from a predetermined height onto a set of

rubber springs and a loading disk which are located

on the top surface of the test specimen prior to the

impact. Transducers mounted in the loading disk shall

monitor the force – time history and displacement –

time history of the loading disk. This data shall be re-

corded with the aid of a data acquisition system.

4.1.2 Test B - Top friction: A slider is pulled hori-

zontally upon the surface of a specimen balance beam

FIG International Gymnastics Federation

Standard Specification for Balance Beams

WAG – Women Artistic Gymnastics

at a defined loading rate. A transducer connected to

the pulling string shall monitor the maximum traction

force generated during the pulling movement.

4.2 Data obtained during these procedures are in-

dicative of the elastic and shock absorbing properties

and the top friction characteristics of balance beams

used in training and FIG-sanctioned competitions.

5 Performance Requirements

5.1 Test A – Elasticity and Shock absorption: When

tested according to the procedures described in Sec-

tion 9.1, the values of the measured variables shall be

within the figures of Table 1.

5.2 Test B – Top friction: When tested according to

the procedures described in Section 9.2, the mean

values of the measured variables shall be within the

figures of Table 2.

Table 1: Figures for Test A – Elasticity and shock ab-

sorption of balance beams

See Figure 2 for an illustration of the impact sites.

x represents the mean values of the measured variables

IV

WAG 3

01.12.1994

2

Table 2: Figures for Test B – Top friction of balance

beam

See Figure 3 for an illustration of the test sites.

x represents the mean value of the measured variable

Test B : Top friction of balance beam

Friction coefficient of balance beam

Mean value across

test sites 1 to 3

Difference between

highest and lowest

mean value on test

sites 1 to 3

Difference between

mean values of

orthogonal test

directions

0.35 ≤x ≤0.60

≤0.05

≤0.05

impact test machine shall meet the following re-

quirements (see Figure 1).

Figure 1: Setup of the loading system

Guide pipe

Impactor

Rubber springs

Loading disk

& Load Cell

Test A : Elasticity and shock absorption of

balance beam

Dmax

(mm)

Mean value

across impact

sites 1 to 7

Difference

between high-

est and lowest

mean value on

impact sites 1

to 7

3.5 ≤x

≤

E

(Nm)

2.5 ≤x

≤9.5

Dr

(mm)

3.0 ≤x

≤20.0

DrVr

(mm2/s)

300 ≤x

≤4800

≤5.0

≤3.0

≤5.0

≤2400

Balance beam

6 Test Apparatus

6.1 Test A – Elasticity and Shock absorption of

balance beam:

6.1.1 Impact test machine: Any type of dynamic

testing apparatus that is capable of impacting a test

specimen using the prescribed loading condition and

monitoring and recording the force - time history and

deflection - time history of the loading disk is accept-

able. The impact test machine shall have sufficient

rigidity to eliminate undesirable vibrations in the ap-

paratus which might be recorded on the force - time

curve and deflection - time curve. The impact test

machine shall also be designed in such a manner that

only the bottom surface of the loading disk contacts

the test specimen at any time during the test proce-

dures.

6.1.2 Loading system - The loading system of the

6.1.2.1 Characteristics of the dynamic load: The

maximum dynamic force shall be 1300 N ±2 % when

this loading system is applied to the testing anvil. The

time from the onset of force application to the time of

maximum force shall be 50 ms ±2 ms.

6.1.2.2 Impactor: The dropping impactor shall be

15 kg ±0.1 kg and shall have a flat impact face. The

impactor shall have the shape of a thick cylinder and

shall be dropped along a guide pipe. The decision of

the size of outside and inside diameters of the impac-

tor is at the discretion of the test laboratory, but the

clearance between the inside hole of the impactor and

the guide pipe shall be 2 mm ±0.2 mm. The dropping

height of the impactor shall be 120 mm ±1 mm to the

upper surface of the rubber springs.

6.1.2.3 Release mechanism: The release mechanism

shall be unattached to the loading disk and the guide

pipe to prevent an additional load with the attached

impactor on the loading disc and the test specimen

FIG International Gymnastics Federation

Standard Specification for Balance Beams

WAG – Women Artistic Gymnastics

before the impact.

6.1.2.4 Loading disk and guide pipe: The loading

disk shall have a diameter of 70 mm ±0.5 mm. The

total mass of the loading disk including the force

transducer and the guide pipe shall be 5 kg ±0.2 kg.

6.1.2.5 Rubber springs: A set of rubber springs

shall be selected so as to meet the requirements de-

scribed in 6.1.2.1.

6.1.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.1.3.1 Force - time: The selection of the specific

force - time recording equipment, including transduc-

ers and recorders, is at the discretion of the test labo-

ratory. However, the recording system shall have a

frequency response adequate to measure the peak

force value to an accuracy of ±3% of the true value.

The total system, detection and recording, shall be

capable of measuring impact forces of up to 2000 N

at frequencies from 2 to 1000 Hz to an accuracy of ±

3%. The minimum sampling rate of the data acquisi-

tion system shall be 5000 Hz.

6.1.3.2 Displacement - time: The selection of the

specific displacement - time recording equipment, in-

cluding transducers and recorders, is at the discretion

of the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the dynamic displacement value to an accuracy of ±

3% of the true value. The total system, detection and

recording, shall be capable of measuring the dis-

placement of ±50 mm at frequencies from 2 to

1000 Hz to an accuracy of ±3%. The minimum sam-

pling rate of the data acquisition system shall be

5000 Hz.

6.1.3.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

6.2 Test B - Top friction of the balance beam:

6.2.1 Measurement device: Any type of friction

testing apparatus that is capable of pulling a slider on

the surface of a specimen balance beam at a the re-

quired test velocity is acceptable. During the test, the

traction force – time history of the slider shall be

monitored and recorded.

6.2.2 Slider: The slider shall have a mass of

5 kg ± 0.2 kg. A square-shaped test sole with a thick-

ness of 10mm ± 0.5 mm and a size of 40 mm ± 1 mm

shall be bonded to the bottom of the slider. The thick-

ness of the test sole shall be decreased to 75% ± 5%

of the original thickness at a pressure of 5 N/cm2. The

coefficient of static friction of the test sole shall be

IV

WAG 3

01.12.1994

3

0.25 ± 0.03.

6.2.3 The slider shall be pulled at a constant load-

ing rate of 5 N/s ± 0.5 N/s.

6.2.4 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.2.4.1 Force - time: The selection of the specific

force - time recording equipment, including trans-

ducer and recorder, is at the discretion of the test

laboratory. The total system, detection and recording,

shall be capable of measuring traction forces up to

100 N at frequencies from 2 to 100 Hz to an accuracy

of ± 3%. The minimum sampling rate of the data ac-

quisition system shall be 200 Hz.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of a complete balance beam as it is intended to

be used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-WAG3.

8 Conditioning and Test Temperature

8.1 The test specimen shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9 Laboratory Procedure (Test Method)

9.1 Test A – Elasticity and Shock absorption of the

balance beam:

9.1.1 Impact sites: A total of seven impact sites

shall be designated on the test specimen. See Figure 2

for an illustration of the impact sites.

Figure 2: Impact sites on the balance beam (dis-

tances in mm)

100

1400

1000

1000

1400

100

1

2

3

4

5

6

7

2, 6 : intersections of beam and legs

9.1.2 Impact test procedures:

9.1.2.1 Place the test specimen under the impact

test machine on a smooth, solid and horizontal floor

(concrete or metal plate) and orient the loading disk

such that the centre of the loading disk contacts one of

the designated impact test sites.

9.1.2.2 Raise the impactor to an appropriate drop

height such that it will impact on the rubber springs

FIG International Gymnastics Federation

Standard Specification for Balance Beams

WAG – Women Artistic Gymnastics

and generate the proper dynamic load described in

Section 6.1.2.

9.1.2.3 Release the impactor and capture the force -

time history and displacement - time history using the

recording equipment described in Section 6.1.3.

9.1.2.4 Upon completion of a given impact test,

raise the impactor off the loading disk.

9.1.2.5 The duration between tests at a given impact

site shall not be less than 120 seconds.

9.1.2.6 Impact each of the seven impact sites five

times. Each test specimen shall receive a total of 35

impacts.

9.1.3 Calculations:

9.1.3.1 Immediately following each test, record the

following measurements: Dmax (mm), E (Nm), Dr

(mm) and DrVr (mm2/s).

9.1.3.2 Determine the arithmetic mean values of the

measured variables for each impact site and for the

overall mean values of the measured variables across

all impact sites. Determine also the differences be-

tween the highest and lowest mean values of the

measured variables for each test site and across all

test sites.

9.2 Test B – Top friction of the balance beam:

9.2.1 Test sites and directions: A total of three test

sites shall be designated on the test specimen as illus-

trated in Figure 3. Four orthogonal test directions for

the traction of the slider shall be also designated on

each test site as illustrated in Figure 3.

Figure 3: Top friction test sites and directions on the

balance beam (distances in mm)

1250

1250

1250

1250

IV

WAG 3

01.12.1994

4

one of the designated test directions. Just before put-

ting the slider on the test specimen, magnesium car-

bonate powder of 1g shall be spread on the surface of

the test site each time.

9.2.2.3 Pull the slider horizontally at a constant

loading rate of 5 N/s ± 0.5 N/s and record the traction

force – time history using recording equipment de-

scribed in Section 6.2.4.

9.2.2.4 Repeat the procedure given in 9.2.2.2 and

9.2.2.3 five times at each test site and in each test di-

rection.

9.2.2.5 Each test specimen shall receive a total of

60 friction test procedures.

9.2.3 Calculations:

9.2.3.1 Immediately following each test, record the

friction coefficient.

9.2.3.2 Determine the overall mean value of the

friction coefficient across the test sites 1 to 3. Deter-

mine also the difference between the highest and the

lowest mean value of the friction coefficient between

all test sites, and the difference between the mean

values of the friction coefficients of the orthogonal

test directions between all test sites.

9.3 Calculate the values of all required variables

rounded to the decimal places of the corresponding

figures identified in Section 5.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested balance

beam, including type, source, manufacturer’s model

number (if appropriate), dimensions of test specimen,

and any other pertinent information. Photographs may

be included in the test report for sample documenta-

tion purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Identification of performed parts of the test –

Test A and Test B.

10.1.6 Description of the impactor mass and the

drop height conditions (Test A), mass and loading

rate of the slider (Test B). A sample loading rate

curve may be included in the test report to indicate

compliance with the loading requirements of 6.1.2.1.

10.1.7 Description of all test results related to the

performance requirements identified in Section 5.

10.1.8 Supplemental description of the test results:

10.1.8.1 Maximum value, minimum value and stan-

1

2

3

Longitudinal Direction

Lateral Direction

9.2.2 Friction test procedures:

9.2.2.1 Place the complete test specimen on a

smooth, solid and horizontal floor.

9.2.2.2 Place the slider on the test specimen in such

a manner that the centre of its sole will contact one of

the designated test sites, and also in such a manner

that the pulling direction of the slider will conform to

FIG International Gymnastics Federation

Standard Specification for Balance Beams

WAG – Women Artistic Gymnastics

dard deviation of Dmax, E, Dr and DrVr variables ac-

cording to Test A.

10.1.8.2 Mean values of Dmax, E, Dr and DrVr vari-

ables at each impact site according to Test A.

10.1.8.3 Dmax, E, Dr and DrVr values for all tests ac-

cording to Test A.

IV

WAG 3

01.12.1994

5

10.1.8.4 Mean values and standard deviations of the

friction coefficients at each test site and in each direc-

tion according to Test B.

10.1.8.5 Friction coefficient values for all tests ac-

cording to Test B.

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

6

FIG International Gymnastics Federation

Standard Specification for Floors

WAG – Women Artistic Gymnastics

Standard Specification: Floors for Women Artistic Gymnastics

IV

WAG 4

01.01.2006

1

This standard is issued under the fixed designation FIG: IV-WAG4-01.01.1997; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

The standard specifications for floors for women artistic gymnastics are the same as for men

artistic gymnastics, therefore, this standard refers to the FIG standard IV-MAG1.

See:

IV

MAG 1

01.01.2006

1-3

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

FIG International Gymnastics Federation

Standard Specification for 20 cm Landing Mats

WAG – Women Artistic Gymnastics

IV

WAG 11

01.08.1996

1

FIG International Gymnastics Federation

Standard Specification for 20 cm Landing Mats

WAG – Women Artistic Gymnastics

IV

WAG 11

01.08.1996

1

Standard Specification: 20 cm Landing Mats for Women Artistic

Gymnastics

This standard is issued under the fixed designation FIG: IV-WAG11-01.08.1996; the numbers immediately fol-

lowing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last

revision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test

laboratories. This standard was originally published in English only. Copyright FIG.

The standard specifications for 20 cm landing mats for women artistic gymnastics are the

same as for men artistic gymnastics, therefore, this standard refers to the FIG standard IV-

MAG11.

IV

See:MAG 11

01.08.1996

1-3

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

2

FIG International Gymnastics Federation

Standard Specification for Vaulting Boards

WAG – Women Artistic Gymnastics

Standard Specification:

Gymnastics

Vaulting

Boards

for

Women

IV

WAG 14

01.01.2006

1

Artistic

This standard is issued under the fixed designation FIG: IV-WAG14-01.07.1985; the numbers immediately fol-

lowing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last

revision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test

laboratories. This standard was originally published in English only. Copyright FIG.

The standard specifications for vaulting boards for women artistic gymnastics are the same as

for men artistic gymnastics, therefore, this standard refers to the FIG standard IV-MAG14.

See:

IV

MAG 14

01.01.2006

1-3

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

2

FIG International Gymnastics Federation

Standard Specification for Rhythmic Gymnastic Floors

RG – Rhythmic Gymnastics

Standard Specification: Rhythmic Gymnastic Floors

IV

RG 1

01.12.1992

1

This standard is issued under the fixed designation FIG: IV-RG1-01.12.1992; the numbers immediately following

the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last revi-

sion. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labora-

tories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of rhythmic

gymnastic floors and to minimize any differences be-

tween competition and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain shock-absorbing, static stiffness and top fric-

tion characteristics of rhythmic gymnastic floors. This

standard specification is applicable to all rhythmic

gymnastic floors that are to be used at any FIG-

sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a rhythmic gymnastic

floor which complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-RG1.

2.2 European Standard: CEN 12503-5: Sport Mats

– Determination of the Base Friction. 2000.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Base plane: The starting reference plane of

the rhythmic gymnastic floor from which the total de-

flection and total height of rebound is determined. It

is taken as the top plane of the test specimen.

3.1.3 Dynamic deflection: The measured distance

(in mm) between the base plane and the maximum

displacement of the impactor below the base plane.

3.1.4 Force (F): The product of the mass of the im-

pactor, expressed in kg and the acceleration of the

impactor, expressed in m/s2.

3.1.5 Maximum Force (Fmax): The maximum value

of force measured during the impact expressed in

Newtons.

3.1.6 Height of rebound: The measured distance (in

mm) between the base plane and the maximum dis-

placement of the impactor above the base plane.

3.1.7 Impactor: The striking part of the test appara-

tus.

3.1.8 Impact velocity: The velocity of the impactor,

expressed in m/s, immediately prior to crossing the

base plane on impact.

3.1.9 Theoretical drop height: A calculated drop

height which equates the measured velocity of the im-

pactor at the moment of dynamic impact to a height

that would generate the same velocity if the test were

performed at sea level and there was no friction to re-

tard the impactor during a drop from that height.

3.1.10 Static deflection: The measured distance be-

tween the base plane and the displacement of the

floor’s surface at a defined distance from the centre of

static indentation. Values are expressed as a percent-

age of the maximum deflection at the centre of inden-

tation.

3.1.11 Slider: A test body of given mass and ge-

ometry. The slider includes a test sole which is

bonded to the bottom of the slider and is made of syn-

thetic material with defined friction properties.

3.1.12 Thrust - traction sequence: A series of 5

successive thrust and traction movements of the slider

which is pushed and pulled horizontally on the sur-

face of the test specimen at a defined speed and dis-

tance.

3.1.13 Sliding distance: The horizontal distance be-

tween the two turning points of the movement of the

slider in a thrust – traction sequence.

3.1.14 Mean thrust - traction force: Mean value of

the absolute, average force, expressed in Newtons, as

the slider moves during the fifth push and pull move-

ment in a thrust - traction sequence.

3.1.15 Friction coefficient: Quotient of the mean

thrust - traction force (in N) and the weight of the

slider (in N) in a thrust - traction sequence.

3.1.16 Base temperature: The surface temperature

(in 0 C) of the test specimen immediately before the

beginning of a thrust - traction sequence.

3.1.17 Mean thrust - traction temperature: Mean

value of the surface temperature (in 0 C) of the test

FIG International Gymnastics Federation

Standard Specification for Rhythmic Gymnastic Floors

RG – Rhythmic Gymnastics

specimen at a defined distance to the slider during the

fifth push and pull movement in a thrust - traction se-

quence.

3.1.18 Temperature rise: Difference (in 0 C) be-

tween the base temperature and the mean thrust - trac-

tion temperature in a thrust - traction sequence.

3.1.19 Orthogonal difference of friction coeffi-

cients: The absolute value of the difference between

the mean value of the friction coefficients of 3 con-

secutive thrust - traction sequences in one measure-

ment direction and the corresponding mean value of 3

additional consecutive thrust - traction sequences in a

perpendicular measurement direction.

3.1.20 Orthogonal difference of temperature rises:

The absolute value of the difference between the

mean value of the temperature rises of 3 consecutive

thrust - traction sequences in one measurement direc-

tion and the corresponding mean value of 3 additional

consecutive thrust - traction sequences in a perpen-

dicular measurement direction.

4 Principles of Measurement

4.1 The complete test procedures include 3 parts:

Determination of shock absorption, determination of

static stiffness and determination of top friction.

4.1.1 Test A - Determination of shock absorption:

A test specimen is impacted with an impactor of given

mass and geometry at a specified velocity. A trans-

ducer mounted in the impactor monitors the accelera-

tion – time history of the impactor which is recorded

with the aid of a data acquisition system. An addi-

tional transducer may be used to monitor the dis-

placement – time history of the impactor.

4.1.2 Test B - Determination of static stiffness: A

static load is applied to the rhythmic gymnastic floor

to obtain an area of impression. The static deflection

of the specimen's surface at defined distances from

the centre of indentation is measured.

4.1.3 Test C - Determination of top friction: A

slider of given mass and geometry traverses the test

specimen which is fixed on a plane surface. The slider

is pushed forward and pulled backwards for a speci-

fied number of times with a constant velocity over a

given distance. Two transducers are mounted at the

slider. One of them monitors the thrust and traction

force - time history of the slider movement. The other

captures the temperature - time history of the surface

of the test piece in a defined distance to the slider.

4.2 Data obtained during these procedures are in-

dicative of the cushioning and rebound properties, the

static stiffness and the top friction characteristics of

the rhythmic gymnastic floor used in training and

FIG-sanctioned competitions.

IV

RG 1

01.12.1992

2

5 Performance Requirements

5.1 Test A - Determination of shock absorption:

When tested according to the procedures described in

Section 9.1, the overall mean value of the measured

variables across all impact sites shall be within the

figures of Table 1.

Table 1: Figures for Test A - Determination of Shock

Absorption

x represents the mean value of the measured variable

Dynamic de-

flection (mm)

21 <= x <= 27

Height of rebound

(mm)

120 <= x <= 180

Fmax

(N)

≤3700

5.2 Test B - Determination of static stiffness:

When tested according to the procedures described in

Section 9.2, the measured variables shall be within the

figures of Table 2.

Table 2: Figures for Test B - Determination of Static

Stiffness

Distance to the centre of

static indentation (cm)

Static deflection (%)

Distance to the centre of

static indentation (cm)

Static deflection (%)

0

100

18

<20

5

100

20

<17

6

<57

22

<14

8

<46

24

<12

10

<38

26

<11

12

<33

28

<9

14

<28

30

<8

16

<24

32

<8

5.3 Test C - Determination of top friction: When

tested according to the procedures described in Sec-

tion 9.3, the measured variables shall be within the

figures of Table 3.

Table 3: Figures for Test C - Determination of Top Fric-

tion

X represents the mean value of the measured variable

Friction

coefficient

Temperature

rise (oC)

Orthogonal

difference of

friction coef-

ficients

≤0.08

Orthogonal

difference of

temperature

rises (0C)

≤0.8

0.32≤ x ≤

≤2.3

6 Test Set-up and Test Apparatus

6.1 Test A - Determination of shock absorption:

6.1.1 Impact test machine: Any type of dynamic

testing apparatus that is capable of impacting a test

specimen at a prescribed impact velocity and monitor-

ing and recording the acceleration - time history of

the impactor is acceptable. The impact test machine

and the impactor shall have sufficient rigidity to

eliminate undesirable vibrations in the apparatus

which might be recorded on the acceleration - time

FIG International Gymnastics Federation

Standard Specification for Rhythmic Gymnastic Floors

RG – Rhythmic Gymnastics

curve. The impact test machine shall also be designed

in such a manner that only the impact face contacts

the test specimen at any time during the test proce-

dures.

6.1.2 Impactor:Theimpactorshallbe

10 kg ± 0.1 kg and shall have a flat impact face with a

10 cm ± 0.5 cm diameter. The edge of the impactor

face should be relieved to eliminate sharp edges. Pro-

vision shall be made so that the accelerometer can be

securely fastened parallel to the vertical axis of the

impactor with a maximum deviation of ±5o.

6.1.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.1.3.1 6.1.3.1 Acceleration - time: The selection of

the specific acceleration - time recording equipment,

including transducers and recorders, is at the discre-

tion of the test laboratory. However, the recording

system shall have a frequency response adequate to

measure the peak acceleration value to an accuracy of

± 5% of the true value. The total system, detection

and recording, shall be capable of measuring impact

accelerations of up to 100 g at frequencies from 2 to

1000 Hz to an accuracy of ± 5%. The minimum sam-

pling rate of the data acquisition system shall be 5000

Hz.

6.1.3.2 6.1.3.2 Displacement - time: It is optional,

but desirable, that the displacement - time history is

recorded by a separate transducer. Any transducer

that provides a linear signal proportional to the dis-

placement of the impactor along the impact axis

which can be monitored coincidentally with the accel-

eration - time trace is acceptable. If displacement is

recorded, the test equipment shall have means to de-

termine and record the top plane (base plane) of the

test specimen from which the total dynamic deflection

and rebound height are determined.

6.1.3.3 6.1.3.3 Filtering: The signal from all trans-

ducers shall be conditioned with a low pass filter

which complies with Channel Class 1000 of SAE

Recommended Practice J211. A fourth-order Butter-

worth low pass filter with a cut-off frequency of 1000

Hz meets this requirement.

6.2 Test B – Determination of static stiffness:

6.2.1 Measurement device: Any type of static test-

ing apparatus that is capable of loading a test speci-

men with a given weight and monitoring and re-

cording the static deflection at defined distances from

the centre of static indentation is acceptable. The test

apparatus, especially the part directly measuring the

deflection, shall also be designed in such a manner

that it does not contact the test specimen in a circular

area of 0.8 m diameter around the centre of indenta-

tion at any time during the test procedures, except the

impact face of the indentor.

6.2.2 Static load: The static load shall be

IV

RG 1

01.12.1992

3

100 kg ± 1 kg, vertically applied by an indentor onto

the test specimen. The indentor shall have a flat im-

pact face with a 10 cm ± 0.5 cm diameter. The edge

of the indentor face should be relieved to eliminate

sharp edges.

6.2.3 Recording equipment for static deflection:

The selection of the specific measurement equipment

is at the discretion of the test laboratory. However, the

means of measuring the static deflection shall have a

flat rectangular contact face of 47 mm * 31 mm ± 3%.

The load on the surface of the test specimen by the

weight of the measuring system shall be 2 N ± 3%.

The accuracy of the system shall be ±0.5 mm.

6.3 Test C – Determination of top friction:

6.3.1 Measurement device: Any type of friction

testing apparatus that is capable of stressing a test

specimen by pushing and pulling a slider on the speci-

men’s surface at a given velocity and distance is ac-

ceptable. During the test the force – time history of

the movement of the slider and the temperature – time

history at the floor’s surface shall be monitored and

recorded. The friction test machine and the slider

shall have sufficient rigidity to eliminate undesirable

vibrations in the apparatus which might be recorded

on the force - time curve. It is desirable to fix the test

specimen for the friction tests with the help of an ad-

ditional fastening system outside the sliding area.

6.3.2 Slider: The slider shall be made of wood with

a mass of 9.5 kg ±3% and shall have the geometrical

dimensions specified in Figure 1. A test sole of syn-

thetic material with a thickness of 2.6 mm ±0.5 mm

shall be bonded to the bottom of the slider, complying

with the requirements of CEN 12503-5:

α:= 47.5 ±0.5. The temperature of the test speci-

men’s surface shall be captured at a distance of

160 mm ±20 mm to front edge of the flat part of the

bottom of the slider (see Figure 1).

Figure 1: Slider Dimensions for Top Friction Tests

of Rhythmic Gymnastic Floors.

(Dimensions in mm; Accuracy: ±mm)

6.3.3 The slider shall be pushed and pulled over a

FIG International Gymnastics Federation

Standard Specification for Rhythmic Gymnastic Floors

RG – Rhythmic Gymnastics

determined sliding distance a specified number of

times at a given constant velocity.

6.3.4 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.3.4.1 Force – time: The selection of the specific

force - time recording equipment, including trans-

ducer and recorder, is at the discretion of the test

laboratory. The total system, detection and recording,

shall be capable of measuring thrust and traction

forces up to ±1000 N at frequencies from 2 to 100

Hz to an accuracy of ± 3%. The minimum sampling

rate of the data acquisition system shall be 200 Hz.

6.3.4.2 Temperature – time: The selection of the

specific temperature - time recording equipment, in-

cluding transducer and recorder, is at the discretion of

the test laboratory. The transducer should have means

to provide temperature measurements during sliding

movements up to 300 mm/s. The time constant of the

temperature transducer shall be T99 ≤4 s. The ther-

moelectric transducer ANRITSU/AIRFLOW C423

meets these requirements. The total system, detection

and recording, shall be capable of measuring tempera-

ture differences up to +100 C at frequencies from 2 to

100 Hz to an accuracy of ± 1%. The minimum sam-

pling rate of the data acquisition system shall be 200

Hz.

7 Test Specimen

7.1 The test specimen submitted for testing shall

represent the rhythmic gymnastic floor as it is in-

tended to be used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-RG1. Exception: See 7.3.

7.3 The minimum horizontal dimensions (length *

width) for any test specimen shall be 200 cm *

120 cm. For Test C (Determination of top friction) the

minimum horizontal dimensions (length * width) for

any test specimen shall be 100 cm * 120 cm.

8 Conditioning and Test Temperature

8.1 The test specimen shall be preconditioned at

50% ± 10% relative humidity and 21o ± 3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9 Laboratory Procedures (Test Methods)

9.1 Test A - Determination of shock absorption:

9.1.1 Impact locations: A total of nine impact sites

shall be designated on the test specimen. See Figure 2

for an illustration of the impact sites.

IV

RG 1

01.12.1992

4

Figure 2: Impact Locations for Rhythmic Gymnastic

Floors

9.1.2 Impact test procedures:

9.1.2.1 9.1.2.1 Place the test specimen under the

impact test machine on a smooth, solid floor (concrete

or metal plate) and orient the impactor such that the

centre of the impact face will contact one of the des-

ignated impact test sites.

9.1.2.2 9.1.2.2 Raise the impactor to an appropriate

drop height such that it will contact the test specimen

with an impact velocity of 2.80 m/s ± 3 %. This cor-

responds to a theoretical drop height of 0.4 m.

9.1.2.3 9.1.2.3 Release the impactor and capture the

acceleration - time history and displacement - time

history (if applicable) using recording equipment de-

scribed in Section 6.1.3.

9.1.2.4 9.1.2.4 Upon completion of a given impact

test, raise the impactor off the surface of the test

specimen.

9.1.2.5 9.1.2.5 The duration between tests at a

given impact site shall not be less than 120 seconds.

9.1.2.6 9.1.2.6 Each test specimen shall receive a

total of 90 impacts. Impact each of the nine impact

sites ten times.

9.1.3 Calculations:

9.1.3.1 9.1.3.1 Immediately following each test, re-

cord the following measurements: Fmax (N), Dynamic

deflection (mm) and Height of rebound (mm).

9.1.3.2 9.1.3.2 The last eight tests for each impact

site shall be used to determine the arithmetic mean

value of a measured variable for each impact site and

for the overall mean value of a measured variable

across all impact sites.

9.2 Test B - Determination of static stiffness:

9.2.1 Static impact test procedure:

9.2.1.1 9.2.2.1 Place the test specimen under the

impact test machine and orient the impactor such that

it will contact the midpoint of the test specimen’s sur-

face. The test specimen shall lie on a smooth, solid

floor (concrete or metal plate) for the test.

9.2.1.2 9.2.2.2 Apply the load on the test speci-

men’s surface for 30 s. Measure and calculate the

static deflection at the following distances from the

centre of indentation: 0 cm; 5 cm; 6 cm; 8 cm; 10 cm;

FIG International Gymnastics Federation

Standard Specification for Rhythmic Gymnastic Floors

RG – Rhythmic Gymnastics

12 cm; 14 cm; 16 cm; 18 cm; 20 cm; 22 cm; 24 cm;

26 cm; 28 cm; 30 cm and 32 cm.

9.2.1.3 9.2.2.3 Upon completion of the measure-

ments unload the surface of the test specimen.

9.3 Test C - Determination of top friction:

9.3.1 Place the test specimen under the slider. Fix

all components carefully with the fastening system to

prevent horizontal movement of the test specimen

during the friction test. The complete test specimen

shall lie on a smooth and solid horizontal plate.

9.3.2 The slider shall be pushed and pulled with a

constant velocity of 300 mm/s ±3% over 90% of the

total sliding distance of 600 mm ±3%.

9.3.3 Perform a thrust – traction sequence with the

slider (i.e. 5 pushing and pulling movements) within

30 sec. Capture the force – time history using re-

cording equipment described in Section 6.3.4. Wait at

least 300 seconds between trials. Repeat the whole

thrust – traction sequence an additional two times

with the pause between trials.

9.3.4 Repeat the procedure given in 9.3.3 to obtain

readings in the perpendicular direction by rotating the

test specimen through 900.

9.3.5 Upon completion of the measurements unload

the surface of the test specimen.

9.3.6 Each test specimen shall receive a total of 6

thrust – traction sequences.

9.3.7 Calculations:

9.3.7.1 9.3.7.1 Immediately following the test, re-

cord and calculate the following measurements for

every thrust – traction sequence: Friction coefficient

and Temperature rise (0 C).

9.3.7.2 9.3.7.2 Determine the overall mean value of

the measured variables for all thrust – traction se-

quences, the Orthogonal difference of friction coeffi-

cients and the Orthogonal difference of temperature

rises.

9.4 Calculate the values of all required variables

rounded to the decimal places of the corresponding

figures identified in Section 5.

IV

RG 1

01.12.1992

5

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested rhyth-

mic gymnastic floor, including type, source, manufac-

turer’s model number (if appropriate), dimensions of

test specimen, and any other pertinent information.

Photographs may be included in the test report for

sample documentation purposes.

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Identification of performed parts of the test –

Test A; Test B; Test C.

10.1.6 Description of the impactor mass and the

drop height conditions (Test A), static load (Test B),

mass, velocity and sliding distance of the slider (Test

C).

10.1.7 Description of the test results relative to the

performance requirements identified in Section 5.

10.1.8 Mean values of Deflection, Height of re-

bound and Fmax across all impact sites according to

Test A.

10.1.9 Maximum value, minimum value and stan-

dard deviation of Deflection, Height of rebound and

Fmax variables according to Test A.

10.1.10 Mean values of Deflection, Height of re-

bound and Fmax for the last eight tests at each impact

site according to Test A.

10.1.11 Deflection, Height of rebound and Fmax

values for all tests according to Test A.

10.1.12 Friction coefficient, temperature rise, Or-

thogonal difference of friction coefficients and Or-

thogonal difference of temperature rises for all thrust

– traction sequences according to test C.

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

6

FIG International Gymnastics Federation

Standard Specification for Floors

AER – Sports Aerobics

Standard Specification: Floors for Sports Aerobics

IV

AER 1

01.07.2000

1

This standard is issued under the fixed designation FIG: IV-AER1-01.07.2000; the numbers immediately follow-

ing the designation indicate the date of original adoption the FIG or, in case of revision, the date of the last revi-

sion. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labora-

tories. This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of sports aerobic

floors and to minimize any differences between com-

petition and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain elastic and shock absorbing characteristics of

sports aerobic floors. This standard specification is

applicable to all sports aerobic floors that are to be

used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a sports aerobic floor

which complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-AER1.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Base plane: The starting reference plane of

the sports aerobic floor from which deflection is de-

termined. It is taken as the upper surface of the floor

loaded by the loading disk prior to any impact.

3.1.2 Deflection (D): The measured distance (in

mm) between the base plane and the bottom surface

of the loading disk during the impact.

3.1.3 Maximum deflection (Dmax): The maximum

value of deflection (in mm) measured during the im-

pact.

3.1.4 Force (F): The force applied to the sports

aerobic floor during the impact, expressed in New-

tons.

3.1.5 Energy of deflection (E): The integration

value or calculated area under the force-deflection

curve expressed in Nm (Newton*meter). The domain

of integration is from the rising point to the maximum

point of deflection on the curve.

3.1.6 Rebound deflection (Dr): The maximum re-

bounding displacement (in mm) of the bottom surface

of the loading disk, measured from the plane of

maximum deflection.

3.1.7 Rebound time: The difference in time (in s)

between the point of maximum deflection and the

point of rebound deflection.

3.1.8 Rebound velocity (Vr): The quotient of re-

bound deflection and rebound time expressed in

mm/s.

3.1.9 Intensity of rebound (DrVr): The product of

rebound deflection and rebound velocity expressed in

mm2/s.

3.1.10 Loading disk: The part of the test apparatus

which applies the specified load to the test specimen.

4 Principle of Measurement

4.1 A specimen sports aerobic floor is impacted by

dropping an impactor from a predetermined height

onto a set of rubber springs and a loading disk which

are located on the top surface of the test specimen

prior to the impact. Transducers mounted in the load-

ing disk shall monitor the force – time history and

displacement – time history of the loading disk. This

data shall be recorded with the aid of a data acquisi-

tion system.

4.2 Data obtained during these procedures are in-

dicative of the elastic and shock absorbing properties

of sports aerobic floors used in training and FIG-

sanctioned competitions.

5 Performance Requirements

5.1 When tested according to the procedures de-

scribed in Section 9, the values of the measured vari-

ables shall be within the figures of Table 1.

FIG International Gymnastics Federation

Standard Specification for Floors

AER – Sports Aerobics

Table 1: Figures for elasticity and shock absorption of

sports aerobic floors

See Figure 2 for an illustration of the impact sites.

x represents the mean values of the measured variables

Dmax

(mm)

Mean value

across impact

sites 1 to 9

Difference

between high-

est and lowest

mean values

on impact sites

1 to 9

3.5 ≤x

≤

E

(Nm)

2.5 ≤x

≤9.5

Dr

(mm)

3.0 ≤x

≤15.0

DrVr

(mm2/s)

300 ≤x

≤3600

IV

AER 1

01.07.2000

2

5.3.4 Loading disk and guide pipe: The loading

disk shall have a diameter of 70 mm ±0.5 mm. The

total mass of the loading disk including the force

transducer and the guide pipe shall be 5 kg ±0.2 kg.

5.3.5 Rubber springs: A set of rubber springs shall

be selected so as to meet the requirements described

in 6.2.1.

Figure 1: Setup of the loading system

Guide pipe

≤5.0

≤3.0

≤5.0

≤2400

Impactor

Rubber springs

Loading disk

& Load cell

Test Apparatus

5.2 Impact test machine: Any type of dynamic test-

ing apparatus that is capable of impacting a test

specimen at a prescribed loading condition and moni-

toring and recording the force - time history and de-

flection - time history of the loading disk is accept-

able. The impact test machine shall have sufficient

rigidity to eliminate undesirable vibrations in the ap-

paratus which might be recorded on the force - time

curve and deflection - time curve. The impact test

machine shall also be designed in such a manner that

only the bottom surface of the loading disk contacts

the test specimen at any time during the test proce-

dures.

5.3 Loading system - The loading system of the im-

pact test machine shall meet the following require-

ments (see Figure 1):

5.3.1 Characteristics of the dynamic load: The

maximum dynamic force shall be 1300N ±2 % when

this loading system is applied to the testing anvil. The

time from the onset of force application to the time of

maximum force shall be 50 ms ±2 ms.

5.3.2 Impactor: The dropping impactor shall be

15 kg ±0.1 kg and shall have a flat impact face. The

impactor shall have the shape of a thick cylinder and

shall be dropped along a guide pipe. The decision of

the size of outside and inside diameters of the impac-

tor is at the discretion of the test laboratory, but the

clearance between the inside hole of the impactor and

the guide pipe shall be 2 mm ±0.2 mm. The dropping

height of the impactor shall be 120 mm ±1 mm to the

upper surface of the rubber springs.

5.3.3 Release mechanism: The release mechanism

shall be unattached to the loading disk and the guide

pipe to prevent an additional load with the attached

impactor on the loading disc and the test specimen

before the impact.

Floor

5.4 Recording equipment - The recording equip-

ment shall meet the following criteria:

5.4.1 Force - time: The selection of the specific

force - time recording equipment, including transduc-

ers and recorders, is at the discretion of the test labo-

ratory. However, the recording system shall have a

frequency response adequate to measure the peak

force value to an accuracy of ±3% of the true value.

The total system, detection and recording, shall be

capable of measuring impact forces of up to 2000 N

at frequencies from 2 to 1000 Hz to an accuracy of

±3%. The minimum sampling rate of the data acqui-

sition system shall be 5000 Hz.

5.4.2 Displacement - time: The selection of the

specific displacement - time recording equipment, in-

cluding transducers and recorders, is at the discretion

of the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the dynamic displacement value to an accuracy of

±3% of the true value. The total system, detection

and recording, shall be capable of measuring the dis-

placement of ±50 mm at frequencies from 2 to

1000 Hz to an accuracy of ±3%. The minimum sam-

pling rate of the data acquisition system shall be

5000 Hz.

5.4.3 Filtering: The signal from all transducers

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

6 Test Specimen

6.1 The test specimen submitted for testing shall

FIG International Gymnastics Federation

Standard Specification for Floors

AER – Sports Aerobics

represent the sports aerobic floor as it is intended to

be used during training and/or competition.

6.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-AER1. Exception: See 7.3.

6.3 The minimum horizontal dimensions (length *

width) for any test specimen shall be

180 cm * 180 cm. The minimum dimensions shall be

also larger than the dimensions of the basic module of

the floor system.

7 Conditioning and Test Temperature

7.1 The test specimen shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

8 Laboratory Procedure (Test Method)

8.1 Impact sites: A total of nine impact sites shall

be designated on the test specimen. See Figure 2 for

an illustration of the impact sites.

Figure 2: Impact sites on the sports aerobic floor

IV

AER 1

01.07.2000

3

site shall not be less than 120 seconds.

8.2.6 Impact each of the nine impact sites five

times. Each test specimen shall receive a total of 45

impacts.

8.3 Calculations:

8.3.1 Immediately following each test, record the

following measurements: Dmax (mm), E (Nm), Dr

(mm) and DrVr (mm2/s).

8.3.2 Determine the arithmetic mean values of the

measured variables for each impact site and for the

overall mean values of the measured variables across

all impact sites. Determine also the differences be-

tween the highest and lowest mean values of the

measured variables for each test site and across all

test sites.

8.4 Calculate the values of all required variables

rounded to the decimal places of the corresponding

figures identified in Section 5.

9 Report

9.1 The test report shall include the following in-

formation:

9.1.1 Complete identification of the tested sports

aerobic floor, including type, source, manufacturer’s

model number (if appropriate), dimensions of test

specimen, and any other pertinent information. Pho-

tographs may be included in the test report for sample

documentation purposes.

9.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

9.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

9.1.4 Conditions of test, including test date, tem-

perature and humidity.

9.1.5 Description of the impactor mass and the drop

height conditions. A sample loading rate curve may

be included in the test report to indicate compliance

with the loading requirements of 6.2.1.

9.1.6 Description of all test results related to the

performance requirements identified in Section 5.

9.1.7 Supplemental description of the test results:

9.1.7.1 Maximum value, minimum value and stan-

dard deviation of Dmax, E, Dr and DrVr variables.

9.1.7.2 Mean values of Dmax, E, Dr and DrVr vari-

ables at each impact site.

9.1.7.3 Dmax, E, Dr and DrVr values for all tests.

8.2 Impact test procedures:

8.2.1 Place the test specimen under the impact test

machine on a smooth, solid and horizontal floor (con-

crete or metal plate) and orient the loading disk such

that the centre of the loading disk contacts one of the

designated impact test sites.

8.2.2 Raise the impactor to an appropriate drop

height such that it will impact on the rubber springs

and generate the proper dynamic load described in

Section 6.2.

8.2.3 Release the impactor and capture the force -

time history and displacement - time history using the

recording equipment described in Section 6.3.

8.2.4 Upon completion of a given impact test, raise

the impactor off the loading disk.

8.2.5 The duration between tests at a given impact

This standard is subject to revision at any time by the FIG Apparatus Commission. You are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

4

FIG International Gymnastics Federation

Standard Specification for Trampolines

TRA – Trampoline

Standard Specification: Trampolines

IV

TRA 1

01.02.1995

1

This standard is issued under the fixed designation FIG: IV-TRA1-01.02.1995; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories and was adapted from the former International Trampoline Federation (FIT) standard for Trampolines

(FIT Handbook 1998). This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of trampolines

and to minimize any differences between competition

and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain elastic properties of trampolines. This stan-

dard specification is applicable to all competition

trampolines that are to be used at any FIG-sanctioned

event.

1.2 This specification does not imply that an injury

cannot be incurred while using a trampoline which

complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-TRA1.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Base plane: The reference plane of the tram-

poline from which the total deflection and total height

of rebound is determined. It is taken as the plane of

the trampoline bed.

3.1.2 Vertical falling line: The reference line in

space, which corresponds to the vertical trajectory of

a test sphere to the first impact on the trampoline.

3.1.3 Reference point of the test sphere: The bot-

tom point of the test sphere in a defined spatial posi-

tion.

3.1.4 Deflection: The vertically measured distance

(in mm) from the base plane to the reference point of

the test sphere at maximum displacement below the

base plane caused by the first impact.

3.1.5 Height of rebound: The vertically measured

distance (in mm) from the base plane to the reference

point of the test sphere at maximum displacement

above the base plane caused by the first rebound.

3.1.6 Deviation to the side during rebound: The

measured horizontal distance (in mm) between the

vertical falling line and the reference point of the test

sphere at maximum displacement above the base

plane.

4 Principle of Measurement

4.1 The trampoline is impacted from a specified

height with a spherical impactor of given mass and

diameter. The three-dimensional displacement – time

history of the impactor is monitored during the impact

onto the bed and the first rebound after impact.

4.2 Displacement data obtained during these proce-

dures are indicative of the elastic properties of the

trampoline used in training and FIG-sanctioned com-

petitions.

5 Performance Requirements

5.1 When tested according to the procedures de-

scribed in Section 9, the mean value of the measured

variables for each impact site shall be within the fig-

ures of Table 1.

Table 1: Figures for Trampolines

(empty cells in table: no requirements;

x represents the mean value of the measured variable at an impact site)

Measurement

point

1

2

3

4

Deflection (mm)

920 ≤x ≤990

Height of rebound (mm)

3100 ≤x ≤3350

≤3350

≤3350

≤3350

Deviation to the side during rebound

(mm)

1550 ≤x ≤1900

FIG International Gymnastics Federation

Standard Specification for Trampolines

TRA – Trampoline

6 Test Apparatus

6.1 Impact test set-up: Any type of test set-up that

is capable of impacting a trampoline under the pre-

scribed conditions and monitoring and recording the

displacement - time history of the reference point of

the test sphere is acceptable. It is optional, but desir-

able, that the test sphere is released magnetically at

the prescribed drop height. In addition it is recom-

mended to attach safety ropes in order to prevent un-

controlled movement of the test sphere after the first

rebound from the bed of the trampoline. The use of

overhead spotting rigs has been found to be useful for

this purpose.

6.2 Test sphere: The test sphere shall be a metal

sphere with a diameter of 40 cm ± 1 cm and a mass of

60 kg ± 0.5 kg. To attach a magnetic fixation to the

sphere, a flat plated upper section (up to a diameter of

10 cm) is acceptable. To attach safety ropes, two suit-

able fixations at the upper side of the sphere are al-

lowed.

6.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.3.1 Displacement - time: It is at the discretion of

the test laboratory to select a specific instrumentation

to monitor, record and calculate the three-dimensional

displacement of the sphere during impact and first re-

bound. The total system shall be capable of measuring

height of rebound and deviation to the side during re-

bound with an accuracy of ± 1 cm and deflection with

an accuracy of ± 0.5 cm. The requirements can be met

by using at least two video cameras (min. frequency

50 Hz; min. shutter speed 1/500) to capture the

movements of the test sphere above the bed of the

trampoline. The spatial motion of the test sphere can

be calculated by three-dimensional cinematographic

analysis utilizing the DLT - algorithm (Direct Linear

Transformation) or a similar technique. The deflec-

tion may be determined by using one camera and two-

dimensional cinematographic analysis.

7 Test Specimen

7.1 The test specimen submitted for testing shall

consist of a trampoline as it is intended to be used

during training and/or competition with safety pad-

ding and with at least one safety platform.

7.2 The trampoline shall comply with FIG Appara-

tus Rules: II-TRA1.

8 Conditioning and Test Temperature

8.1 The trampoline, mounted and assembled for

use, shall be preconditioned at 50% ± 10% relative

humidity and 21° C ± 3° C for a minimum of 24 hours

prior to the test. All testing shall be carried out under

the same conditions.

IV

TRA 1

01.02.1995

2

9 Laboratory Procedure (Test Method)

9.1 Impact locations: A total of four impact sites

shall be designated on the trampoline. See Figure 1

for an illustration of the impact sites.

9.2 Impact test procedures:

9.2.1 Place the test specimen on a smooth and solid

floor and orient the impact test sphere so that the con-

tact will be at one of the designated impact test sites.

Figure 1: Impact Locations on the Bed for Trampo-

lines with Marked Jumping Zone.

The locations 1 to 4 are the midpoints to related

parts of the bed and the marked out jumping zone.

9.2.2 Raise the test sphere to an appropriate drop

height such that the distance between the reference

point of the test sphere and the unloaded bed of the

trampoline is 400 cm ±2 cm.

9.2.3 Release the test sphere and capture the dis-

placement - time history using recording equipment

described in Section 6.3.

9.2.4 Upon completion of a given impact test, raise

the test sphere off the surface of the trampoline.

9.2.5 Check the displacement recordings after every

test. If there is any deviation during the free fall of the

test sphere (i.e. by pulling at the overhead safety rigs

too early), the test shall be repeated.

9.2.6 Repeat the test procedures such that the tram-

poline to be tested shall receive three impacts at each

of the four impact sites for a total of 12 impacts.

9.3 Calculations:

9.3.1 For each test, calculate the following meas-

urements: Deflection (mm), Height of rebound (mm)

and Deviation to the side during rebound (mm).

9.3.2 All three tests for each impact site shall be

used to determine the arithmetic mean value of a

measured variable for each impact site.

9.3.3 Calculate the mean values of Deflection,

Height of rebound and Deviation to the side during

FIG International Gymnastics Federation

Standard Specification for Trampolines

TRA – Trampoline

rebound across all impact sites rounded to zero deci-

mal places.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested trampo-

line, including type, source, manufacturer’s model

number (if appropriate), dimensions of the trampo-

line, and any other pertinent information. Photographs

may be included in the test report for sample docu-

mentation purposes.

IV

TRA 1

01.02.1995

3

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Description of the test sphere mass and the

drop height conditions.

10.1.6 Description of the test results relative to the

performance requirements identified in Section 5.

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

4

FIG International Gymnastics Federation

Standard Specification for Tumbling Tracks

TRA – Trampoline

Standard Specification: Tumbling Tracks

IV

TRA 3

01.07.1996

1

This standard is issued under the fixed designation FIG: IV-TRA3-01.07.1996; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG, or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories and was adapted from the former International Trampoline Federation (FIT) standard for Tumbling Tracks

(FIT Handbook 1998). This standard was originally published in English only. Copyright FIG.

Introduction

The objective of this FIG standard is to provide equal

opportunities for all athletes in FIG competitions by

controlling the functional properties of tumbling

tracks and to minimize any differences between com-

petition and training equipment.

1 Scope

1.1 This specification covers the measurement of

certain shock-absorbing, rebound, top friction and

stability characteristics of tumbling tracks. This stan-

dard specification is applicable to all tumbling tracks

that are to be used at any FIG-sanctioned event.

1.2 This specification does not imply that an injury

cannot be incurred while using a tumbling track which

complies with this specification.

1.3 The test procedures associated with this stan-

dard may involve hazardous operations and equip-

ment. This standard does not purport to address all

the safety problems associated with its use. It is the

responsibility of the user of this standard to establish

appropriate safety and health practices and to deter-

mine the applicability of regulatory limitations prior

to use.

2 Normative References

2.1 Society of Automotive Engineers: SAE J211

Recommended Practice for Instrumentation for Im-

pact Tests – Requirements for Channel Class 1000,

October 1988.

2.2 International Gymnastics Federation (FIG): Ap-

paratus Rules: II-TRA3.

2.3 European Standard: CEN 12503-5: Sport Mats

– Determination of the Base Friction. 2000.

3 Terminology

3.1 Description of terms specific to this standard:

3.1.1 Acceleration: The instantaneous time rate of

change of velocity, expressed in m/s2, which may be

positive or negative.

3.1.2 Base plane: The starting reference plane of

the tumbling track from which the total height of re-

bound is determined. It is taken as the top plane of the

tumbling track.

3.1.3 Force (F): The product of the mass of the im-

pactor, expressed in kg, and the acceleration of the

impactor, expressed in m/s2.

3.1.4 Maximum Force (Fmax): The maximum value

of force measured during the impact and expressed in

Newtons.

3.1.5 Height of rebound: The calculated distance

(in mm) between the base plane and the maximum

vertical displacement of the impactor above the base

plane under idealized frictionless conditions.

3.1.6 Impactor: The striking part of the test appara-

tus.

3.1.7 Slider: A test body of given mass and geome-

try. The slider includes a test sole which is bonded to

the bottom of the slider and is made of synthetic ma-

terial with defined friction properties.

3.1.8 Thrust - traction sequence: A series of 5 suc-

cessive thrust and traction movements of the slider

which is pushed and pulled horizontally on a surface

of the test specimen at a defined speed and distance.

3.1.9 Sliding distance: The horizontal distance be-

tween the two turning points of the movement of the

slider in a thrust – traction sequence.

3.1.10 Mean thrust - traction force: Mean value of

the absolute, average force, expressed in Newtons, as

the slider moves during the fifth push and pull move-

ment in a thrust - traction sequence.

3.1.11 Friction coefficient: Quotient of the mean

thrust - traction force (in N) and the weight of the

slider (in N) in a thrust - traction sequence.

4 Principles of Measurement

4.1 The complete measurement is composed of two

specific test procedures:

4.1.1 Test A - Impact test: A test specimen is im-

pacted with an impactor of given mass and geometry

from a specified drop height. A transducer mounted

inside the impactor monitors the acceleration – time

history of the impactor which is recorded with the aid

of a data acquisition system.

4.1.2 Test B - Determination of top friction: A

slider of given mass and geometry traverses the test

specimen which is fixed on a plane surface. The slider

is pushed forward and pulled backwards for a speci-

fied number of times with a constant velocity over a

given distance. A transducer mounted at the slider

monitors the thrust and traction force - time history of

the slider movement.

FIG International Gymnastics Federation

Standard Specification for Tumbling Tracks

TRA – Trampoline

4.2 Dynamic data obtained during these procedures

are indicative of the cushioning and rebound (Test A)

and top friction (Test B) properties of tumbling tracks

used in training and FIG-sanctioned competitions.

5 Performance Requirements

5.1 Test A - Impact test: When tested according to

the procedures described in Section 9.1, the overall

mean values of the measured variables across all im-

pact sites shall be within the figures of Table 1.

Table 1: Figures for Test A – Impact Test

Figure 1: Geometry of Impactor

IV

TRA 3

01.07.1996

2

Height of rebound (mm)

≥550

Fmax (N)

≤6500

5.2 Test B - Top friction: When tested according to

the procedures described in Section 9.2, the mean

value of the measured variable shall be within the fig-

ure of Table 2.

Table 2: Figures for Test B – Top Friction

Friction coefficient

≥0.45

6 Test Apparatus

6.1 Test A - Impact test procedures:

6.1.1 Impact test machine: Any type of dynamic

testing apparatus that is capable of impacting a test

specimen with an impactor from a prescribed drop

height and monitoring and recording the acceleration

- time history of the impactor is acceptable. The im-

pact test machine shall be designed in such a manner

that only the impact face contacts the test specimen at

any time during the test procedures. It is optional, but

desirable, that the impactor is released from a magnet.

6.1.2 Impactor: The impactor shall consist of a cy-

lindrical test body with a mass of 30 kg ± 0.3 kg and a

geometry as specified in Figure 1. The accelerometer

shall be rigidly mounted on the impactor as indicated

in Figure 1.

6.1.3 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.1.3.1 Acceleration - time: The selection of the

specific acceleration - time recording equipment, in-

cluding transducer and recorder, is at the discretion of

the test laboratory. However, the recording system

shall have a frequency response adequate to measure

the peak acceleration value to an accuracy of ± 5% of

the true value. The total system, detection and re-

cording, shall be capable of measuring impact accel-

erations of up to 100 g at frequencies from 2 to 1000

Hz to an accuracy of ± 5%. The minimum sampling

rate of the data acquisition system shall be 5000 Hz.

6.1.3.2 Filtering: The signal from the transducer

shall be conditioned with a low pass filter which

complies with Channel Class 1000 of SAE Recom-

mended Practice J211. A fourth-order Butterworth

low pass filter with a cut-off frequency of 1000 Hz

meets this requirement.

6.2 Test B - Top friction:

6.2.1 Measurement device: Any type of friction

testing apparatus that is capable of stressing a test

specimen by pushing and pulling a slider on the test

specimen’s surface at a given velocity and distance is

acceptable. During the test the force – time history of

the movement of the slider shall be monitored and re-

corded. The friction test machine and the slider shall

have sufficient rigidity to eliminate undesirable vibra-

tions in the apparatus which might be recorded on the

force - time curve. It is desirable to fix the test speci-

men for the friction tests with the help of an addi-

FIG International Gymnastics Federation

Standard Specification for Tumbling Tracks

TRA – Trampoline

tional fastening system outside the sliding area.

6.2.2 Slider: The slider shall be made of wood with

a mass of 9.5 kg ± 3% and shall have the geometrical

dimensions specified in Figure 2. A test sole of syn-

thetic material with a thickness of 2.6mm ± 0.5 mm

shall be bonded to the bottom of the slider, complying

with the requirements of CEN 12503-5:

aL := 47.5 ± 0.5.

Figure 2: Slider Dimensions for Top Friction Tests

(Dimensions in mm; Accuracy: ±mm)

IV

TRA 3

01.07.1996

3

9 Laboratory Procedure (Test Method)

9.1 Test A - Impact test:

9.1.1 Impact locations: A total of seven impact

sites shall be designated on the test specimen. See

Figure 3 for an illustration of the impact sites.

9.1.2 Impact test procedures:

9.1.2.1 Place the test specimen under the impact

test machine on a smooth, solid floor (concrete or

metal plate) and orient the impactor such that the cen-

tre of the impact face will contact one of the desig-

nated impact test sites.

9.1.2.2 Raise the impactor to the drop height of

1.20 m ±3%.

9.1.2.3 Release the impactor and capture the accel-

eration - time history using recording equipment de-

scribed in Section 6.1.3.

9.1.2.4 Upon completion of a given impact test,

raise the impactor off the surface of the test specimen.

9.1.2.5 The duration between tests at a given impact

site shall not be less than 120 seconds.

9.1.2.6 Each test specimen shall receive a total of

70 impacts. Impact each of the seven impact sites ten

times.

Figure 3: Impact Locations for Tumbling Tracks

6.2.3 The slider shall be pushed and pulled over a

determined sliding distance a specified number of

times at a given constant velocity.

6.2.4 Recording equipment - The recording equip-

ment shall meet the following criteria:

6.2.4.1 Force – time: The selection of the specific

force - time recording equipment, including trans-

ducer and recorder, is at the discretion of the test

laboratory. The total system, detection and recording,

shall be capable of measuring thrust and traction

forces up to ± 1000 N at frequencies from 2 to 100

Hz to an accuracy of ± 3%. The minimum sampling

rate of the data acquisition system shall be 200 Hz.

7 Test Specimen

7.1 The test specimen submitted for testing shall

represent the tumbling track as it is intended to be

used during training and/or competition.

7.2 The test specimen shall comply with FIG Appa-

ratus Rules: II-TRA3. Exception: See 7.3.

7.3 The minimum horizontal dimensions (width *

length) for any test specimen shall be 170 cm *

120 cm.

8 Conditioning and Test Temperature

8.1 The test specimen shall be preconditioned at

50% ±10% relative humidity and 21o C ±3o C for a

minimum of 24 hours prior to the test. All testing

shall be carried out under the same conditions.

9.1.3 Calculations:

9.1.3.1 Immediately following each test, calculate

and record the following measurements: Fmax (N) and

Height of rebound (mm).

9.1.3.2 The last eight tests for each impact site shall

be used to determine the arithmetic mean value of a

measured variable for each impact site and for the

overall mean value of a measured variable across all

impact sites.

9.2 Test B - Top Friction:

9.2.1 Place the test specimen under the slider. Fix

all components carefully with the fastening system to

FIG International Gymnastics Federation

Standard Specification for Tumbling Tracks

TRA – Trampoline

prevent horizontal movement of the test specimen

during the friction test. The complete test specimen

shall lie on a smooth and solid horizontal plate.

9.2.2 The slider shall be pushed and pulled parallel

to the boundary lines of the tumbling track with a

constant velocity of 300 mm/s ± 3% over 90% of the

total sliding distance of 600 mm ± 3%.

9.2.3 Perform a thrust – traction sequence with the

slider (i.e. 5 pushing and pulling movements) within

30 sec. Capture the force – time history using re-

cording equipment described in Section 6.2.4. Wait at

least 300 seconds between trials. Repeat the whole

thrust – traction sequence an additional two times

with the pause between trials.

9.2.4 Calculations:

9.2.4.1 Immediately following the test, record and

calculate the friction coefficient for every thrust –

traction sequence.

10 Report

10.1 The test report shall include the following in-

formation:

10.1.1 Complete identification of the tested tum-

bling track, including type, source, manufacturer’s

model number (if appropriate), dimensions of test

specimen, and any other pertinent information. Pho-

tographs may be included in the test report for sample

documentation purposes.

IV

TRA 3

01.07.1996

4

10.1.2 Test identification number according to the

internal regulations between the FIG Test Institutes.

10.1.3 Complete identification of the testing labora-

tory including test technician and test laboratory man-

ager (if appropriate).

10.1.4 Conditions of test, including test date, tem-

perature and humidity.

10.1.5 Test A - Impact Test:

10.1.5.1 Description of the impactor mass and the

drop height conditions.

10.1.5.2 Description of the test results relative to

the performance requirements identified in Sec-

tion 5.1.

10.1.5.3 Mean values of height of rebound and Fmax

across all impact sites.

10.1.5.4 Maximum value, minimum value and stan-

dard deviation of height of rebound and Fmax vari-

ables.

10.1.5.5 Mean values of height of rebound and Fmax

for the last eight tests at each impact site

10.1.5.6 Height of rebound and Fmax for all tests.

10.1.6 Test B - Top Friction:

10.1.6.1 Description of the mass, velocity and slid-

ing distance of the slider.

10.1.6.2 Friction coefficients for all thrust – traction

sequences.

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

FIG International Gymnastics Federation

Standard Specification for Vaulting Boards

TRA - Trampoline

Standard Specification: Vaulting Boards for Tumbling

IV

TRA 14

01.01.2006

1

This standard is issued under the fixed designation FIG: IV-ACRO11-01.01.00; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

The standard specifications for vaulting boards for tumbling are the same as for men artistic

gymnastics, therefore, this standard refers to the FIG standard IV-MAG14.

See:

IV

MAG 14

01.01.2006

1-3

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary

IV

2

FIG International Gymnastics Federation

Standard Specification for Floors

ACRO – Acrobatics

Standard Specification: Floors for Acrobatics

IV

ACRO 1

01.01.2006

1

This standard is issued under the fixed designation FIG: IV-ACRO1-01.01.00; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

The standard specifications for floors for acrobatics are the same as for men artistic gymnas-

tics, therefore, this standard refers to the FIG standard IV-MAG1.

See:

IV

MAG 1

01.01.2006

1-3

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary.

IV

2

FIG International Gymnastics Federation

Standard Specification for 20 cm Landing Mats

ACRO - Acrobatics

Standard Specification: 20 cm Landing Mats for Acrobatics

IV

ACRO 11

01.01.2000

1

This standard is issued under the fixed designation FIG: IV-ACRO11-01.01.00; the numbers immediately follow-

ing the designation indicate the date of original adoption by the FIG or, in case of revision, the date of the last re-

vision. This FIG standard was prepared by the Apparatus Commission of the FIG and participating FIG test labo-

ratories. This standard was originally published in English only. Copyright FIG.

The standard specifications for 20 cm landing mats for acrobatics are the same as for men ar-

tistic gymnastics, therefore, this standard refers to the FIG standard IV-MAG11.

See:

IV

MAG 11

01.08.1996

1-3

This standard is subject to revision at any time by the FIG Apparatus Commission. Your are invited to comment

on revision of this standard or on additional standards. Comments should be addressed to the FIG General Secre-

tary